## Slide 1: Memory Systems Fundamentals, Recent Research, Challenges, Opportunities Lecture 5: Emerging Memory Technologies
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
9 October 2018
Technion Fast Course 2018

## Slide 2: Emerging Memory Technologies

## Slide 3: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 4: Solution 1: New Memory Architectures
Overcome memory shortcomings with
  Memory-centric system design
  Novel memory architectures, interfaces, functions
  Better waste management (efficient utilization)
Key issues to tackle
  Enable reliability at low cost  high capacity
  Reduce energy
  Reduce latency
  Improve bandwidth
  Reduce waste (capacity, bandwidth, latency)
  Enable computation close to data

## Slide 5: Solution 1: New Memory Architectures
Liu+, “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices,” ISCA 2013.
Seshadri+, “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
Pekhimenko+, “Linearly Compressed Pages: A Main Memory Compression Framework,” MICRO 2013.
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.
Qureshi+, “AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems,” DSN 2015.
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field,” DSN 2015.
Kim+, “Ramulator: A Fast and Extensible DRAM Simulator,” IEEE CAL 2015.
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM,” IEEE CAL 2015.
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing,” ISCA 2015.
Ahn+, “PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture,” ISCA 2015.
Lee+, “Decoupled Direct Memory Access: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM,” PACT 2015.
Seshadri+, “Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses,” MICRO 2015.
Lee+, “Simultaneous Multi-Layer Access: Improving 3D-Stacked Memory Bandwidth at Low Cost,” TACO 2016.
Hassan+, “ChargeCache: Reducing DRAM Latency by Exploiting Row Access Locality,” HPCA 2016.
Chang+, “Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Migration in DRAM,” HPCA 2016.
Chang+, “Understanding Latency Variation in Modern DRAM Chips Experimental Characterization, Analysis, and Optimization,” SIGMETRICS 2016.
Khan+, “PARBOR: An Efficient System-Level Technique to Detect Data Dependent Failures in DRAM,” DSN 2016.
Hsieh+, “Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems,” ISCA 2016.
Hashemi+, “Accelerating Dependent Cache Misses with an Enhanced Memory Controller,” ISCA 2016.
Boroumand+, “LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory,” IEEE CAL 2016.
Pattnaik+, “Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities,” PACT 2016.
Hsieh+, “Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation,” ICCD 2016.
Hashemi+, “Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads,” MICRO 2016.
Khan+, “A Case for Memory Content-Based Detection and Mitigation of Data-Dependent Failures in DRAM",” IEEE CAL 2016.
Hassan+, “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Mutlu, “The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser,” DATE 2017.
Lee+, “Design-Induced Latency Variation in Modern DRAM Chips: Characterization, Analysis, and Latency Reduction Mechanisms,” SIGMETRICS 2017.
Chang+, “Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms,” SIGMETRICS 2017.
Patel+, “The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions,” ISCA 2017.
Seshadri and Mutlu, “Simple Operations in Memory to Reduce Data Movement,” ADCOM 2017.
Liu+, “Concurrent Data Structures for Near-Memory Computing,” SPAA 2017.
Khan+, “Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content,” MICRO 2017.
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
Kim+, “GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies,” BMC Genomics 2018.
Kim+, “The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices,” HPCA 2018.
Boroumand+, “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018.
Das+, “VRL-DRAM: Improving DRAM Performance via Variable Refresh Latency,” DAC 2018.
Ghose+, “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study,” SIGMETRICS 2018.
Kim+, “Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines,” ICCD 2018.
Wang+, “Reducing DRAM Latency via Charge-Level-Aware Look-Ahead Partial Restoration,” MICRO 2018.
Avoid DRAM:
  Seshadri+, “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.
  Pekhimenko+, “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
  Seshadri+, “The Dirty-Block Index,” ISCA 2014.
  Pekhimenko+, “Exploiting Compressed Block Size as an Indicator of Future Reuse,” HPCA 2015.
  Vijaykumar+, “A Case for Core-Assisted Bottleneck Acceleration in GPUs: Enabling Flexible Data Compression with Assist Warps,” ISCA 2015.
  Pekhimenko+, “Toggle-Aware Bandwidth Compression for GPUs,” HPCA 2016.

## Slide 6: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS 2009])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 7: Solution 2: Emerging Memory Technologies
Lee+, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA’09, CACM’10, IEEE Micro’10.
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Lu+, “Loose Ordering Consistency for Persistent Memory,” ICCD 2014.
Zhao+, “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.
Yoon, Meza+, “Efficient Data Mapping and Buffering Techniques for Multi-Level Cell Phase-Change Memories,” TACO 2014.
Ren+, “ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems,” MICRO 2015.
Chauhan+, “NVMove: Helping Programmers Move to Byte-Based Persistence,” INFLOW 2016.
Li+, “Utility-Based Hybrid Memory Management,” CLUSTER 2017.
Yu+, “Banshee: Bandwidth-Efficient DRAM Caching via Software/Hardware Cooperation,” MICRO 2017.
Tavakkol+, “MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices,” FAST 2018.
Tavakkol+, “FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives,” ISCA 2018.
Sadrosadati+. “LTRF: Enabling High-Capacity Register Files for GPUs via Hardware/Software Cooperative Register Prefetching,” ASPLOS 2018.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 8: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 9: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 10: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 11: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 12: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 13: PCM Resistance → Value
Cell resistance
1
0
Cell value:

## Slide 14: Multi-Level Cell PCM
Multi-level cell: more than 1 bit per cell
  Further increases density by 2 to 4x [Lee+,ISCA'09]
But MLC-PCM also has drawbacks
  Higher latency and energy than single-level cell PCM

## Slide 15: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Bit 1
Bit 0

## Slide 16: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Less margin between values
→ need more precise sensing/modification of cell contents
→ higher latency/energy (~2x for reads and 4x for writes)

## Slide 17: Phase Change Memory Properties
Surveyed prototypes from 2003-2008 (ITRS, IEDM, VLSI, ISSCC)
Derived PCM parameters for F=90nm
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
Lee et al., “Phase Change Technology and the Future of Main Memory,” IEEE Micro Top Picks 2010.

## Slide 19: Phase Change Memory Properties: Latency
Latency comparable to, but slower than DRAM
Read Latency
  50ns: 4x DRAM, 10-3x NAND Flash
Write Latency
  150ns: 12x DRAM
Write Bandwidth
  5-10 MB/s: 0.1x DRAM, 1x NAND Flash
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 20: Phase Change Memory Properties
Dynamic Energy
  40 uA Rd, 150 uA Wr
  2-43x DRAM, 1x NAND Flash
Endurance
  Writes induce phase change at 650C
  Contacts degrade from thermal expansion/contraction
  108 writes per cell
  10-8x DRAM, 103x NAND Flash
Cell Size
  9-12F2 using BJT, single-level cells
  1.5x DRAM, 2-3x NAND (will scale with feature size, MLC)

## Slide 21: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 22: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 23: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 24: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 25: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 26: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 27: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 28: Required Reading: PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 29: More on PCM As Main Memory (II)
Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 30: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 31: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Poor density (currently)
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 32: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Chart: Performance vs. DRAM
STT-RAM (base) | 0.95574 | 0.91812 | 0.93435 | 0.95579 | 0.95738 | 0.92083 | 0.95404 | 0.93019 | 0.95413 | 0.94507 | 0.92103 | 0.94061
STT-RAM (opt) | 0.96014 | 0.91453 | 0.9443 | 0.95632 | 0.95951 | 0.92092 | 0.95948 | 0.93564 | 0.96003 | 0.94574 | 0.93546 | 0.94473
Chart: Energy vs. DRAM
| mpmix0 | mpmix1 | mpmix2 | mpmix3 | mpmix4 | mpmix5 | mpmix6 | mpmix7 | mpmix8 | mpmix9 | mpmix10 | Average
ACT+PRE | 0.30175 | 0.27646 | 0.37425 | 0.32119 | 0.33973 | 0.34883 | 0.36197 | 0.2603 | 0.33524 | 0.39385 | 0.32655 | 0.33092
WB | 0.018529 | 0.027397 | 0.013518 | 0.015979 | 0.022233 | 0.018649 | 0.015872 | 0.025826 | 0.01687 | 0.016362 | 0.015008 | 0.018749
RB | 0.01752 | 0.014162 | 0.010281 | 0.018781 | 0.023665 | 0.010148 | 0.024161 | 0.016986 | 0.013315 | 0.012743 | 0.010166 | 0.01563
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 33: More on STT-MRAM as Main Memory
Emre Kultursay, Mahmut Kandemir, Anand Sivasubramaniam, and Onur Mutlu, "Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative" Proceedings of the 2013 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Austin, TX, April 2013. Slides (pptx) (pdf)

## Slide 34: A More Viable Approach: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 35: Challenge and Opportunity
Providing the Best of
Multiple Metrics
with
Multiple Memory Technologies

## Slide 36: Challenge and Opportunity
Heterogeneous,
Configurable,
Programmable
Memory Systems

## Slide 37: Hybrid Memory Systems: Issues
Cache vs. Main Memory
Granularity of Data Move/Manage-ment: Fine or Coarse
Hardware vs. Software vs. HW/SW Cooperative
When to migrate data?
How to design a scalable and efficient large cache?
…

## Slide 38: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a low-cost hardware-managed DRAM cache?
Two idea directions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 39: DRAM as a Cache for PCM
Goal: Achieve the best of both DRAM and PCM/NVM
  Minimize amount of DRAM w/o sacrificing performance, endurance
  DRAM as cache to tolerate PCM latency and write bandwidth
  PCM as main memory to provide large capacity at good cost and power
DATA
PCM Main Memory
DATA
T
DRAM Buffer
PCM Write Queue
T=Tag-Store
Processor
Flash
Or
HDD
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 40: Write Filtering Techniques
Lazy Write: Pages from disk installed only in DRAM, not PCM
Partial Writes: Only dirty lines from DRAM page written back
Page Bypass: Discard pages with poor reuse on DRAM eviction
Qureshi et al., “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Processor
DATA
PCM Main Memory
DATA
T
DRAM Buffer
Flash
Or
HDD

## Slide 41: Results: DRAM as PCM Cache (I)
Simulation of 16-core system, 8GB DRAM main-memory at 320 cycles, HDD (2 ms) with Flash (32 us) with Flash hit-rate of 99%
Assumption: PCM 4x denser, 4x slower than DRAM
DRAM block size = PCM page size (4kB)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Notes: Workloads:
Database workloads & Data parallel kernels
1. Database workloads: db1 and db2
2. Unix utilities: qsort and binary search
3. Data Mining : K-means and Gauss Seidal
4. Streaming: DAXPY and Vector Dot Product

## Slide 42: Results: DRAM as PCM Cache (II)
PCM-DRAM Hybrid performs similarly to similar-size DRAM
Significant energy savings with PCM-DRAM Hybrid
Average lifetime: 9.7 years (no guarantees)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 43: More on DRAM-PCM Hybrid Memory
Scalable High-Performance Main Memory System Using Phase-Change Memory Technology. Moinuddin K. Qureshi, Viji Srinivasan, and Jude A. Rivers Appears in the International Symposium on Computer Architecture (ISCA) 2009.

## Slide 44: Data Placement in Hybrid Memory
Memory A is fast, but small
Load should be balanced on both channels?
Page migrations have performance and energy overhead
Channel A
Channel B
Memory A
Memory B
(Fast, Small)
(Large, Slow)
Page 1
Page 2
IDLE
Which memory do we place each page in,
to maximize system performance?
Cores/Caches
Memory Controllers

## Slide 45: Data Placement Between DRAM and PCM
Idea: Characterize data access patterns and guide data placement in hybrid memory
Streaming accesses: As fast in PCM as in DRAM
Random accesses: Much faster in DRAM
Idea: Place random access data with some reuse in DRAM; streaming data in PCM
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 46: Key Observation & Idea
Row buffers exist in both DRAM and PCM
  Row hit latency similar in DRAM & PCM [Lee+ ISCA’09]
  Row miss latency small in DRAM, large in PCM
Place data in DRAM which
  is likely to miss in the row buffer (low row buffer locality) miss penalty is smaller in DRAM
  AND
  is reused many times  cache only the data worth the movement cost and DRAM space
Notes: Our key observation is that row buffers exist in both DRAM and PCM.
Row hit latency, which does not access the memory cell array, is similar in DRAM and PCM.
It is for a row miss that the memory access latency is small in DRAM and large in PCM.
Therefore we would like to place data in DRAM which:
Is likely to miss in the row buffer, which we call as having low row buffer locality, since the row buffer miss penalty is small in DRAM than it is in PCM.
And we would like to place data in DRAM which is reused many times, so that we cache only the data that is worth the movement cost.

## Slide 47: Hybrid vs. All-PCM/DRAM [ICCD’12]
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 48: More on Hybrid Memory Data Placement
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf)

## Slide 49: Weaknesses of Existing Solutions
They are all heuristics that consider only a limited part of memory access behavior
Do not directly capture the overall system performance impact of data placement decisions
Example: None capture memory-level parallelism (MLP)
  Number of concurrent memory requests from the same application when a page is accessed
  Affects how much page migration helps performance
Notes: These proposals consider only a limited number of characteristics, using these few data points to construct a placement heuristic that is specific to the memory types being used in the system.
These heuristic-based approaches do not directly capture the overall system performance benefits of data placement decisions.
Therefore, they can only indirectly optimize system performance, which sometimes leads to sub-optimal data placement decisions.

## Slide 50: Importance of Memory-Level Parallelism
requests to Page 1
requests to Page 3
requests to Page 1
requests to Page 3
time
Before migration:
After migration:
requests to Page 2
requests to Page 2
time
Before migration:
After migration:
Mem. B
Mem. B
Mem. A
Mem. A
Mem. B
Mem. A
T
T
Migrating one page reduces stall time by T
Must migrate two pages to reduce stall time by T:
migrating one page alone does not help
Mem. B
Page migration decisions need to consider MLP
Notes: Should say: On the left, The page has much more utility because it directly affects performance if it is migrated to the fast memory;
On the right. Each page has less utility because migrated alone, neither would affect performance significantly. They both need to be migrated together.
Let’s look at two pages with access latency overlapped with each other
Change animation later

## Slide 51: Our Goal [CLUSTER 2017]
A generalized mechanism that
1. Directly estimates the performance benefit of migrating a page between any two types of memory
2. Places only the performance-critical data in the fast memory

## Slide 52: Utility-Based Hybrid Memory Management
A memory manager that works for any hybrid memory
  e.g., DRAM-NVM, DRAM-RLDRAM
Key Idea
  For each page, use comprehensive characteristics to calculate estimated utility (i.e., performance impact) of migrating page from one memory to the other in the system
  Migrate only pages with the highest utility (i.e., pages that improve system performance the most when migrated)
Li+, “Utility-Based Hybrid Memory Management”, CLUSTER 2017.

## Slide 53: Key Mechanisms of UH-MEM
For each page, estimate utility using a performance model
  Application stall time reduction
    How much would migrating a page benefit the performance of the application that the page belongs to?
  Application performance sensitivity
    How much does the improvement of a single application’s performance increase the overall system performance?
Migrate only pages whose utility exceed the migration threshold from slow memory to fast memory
Periodically adjust migration threshold

## Slide 54: Results: System Performance
Chart: Workload Memory Intensity Category
| 0 | 0.25 | 0.5 | 0.75 | 1
ALL | 1 | 1 | 1 | 1 | 1
FREQ | 1.09 | 1.06 | 1.1 | 1.22 | 1.39
RBLA | 1.09 | 1.09 | 1.11 | 1.26 | 1.42
UH-MEM | 1.09 | 1.12 | 1.16 | 1.37 | 1.61
14%
5%
3%
9%
UH-MEM improves system performance
over the best state-of-the-art hybrid memory manager

## Slide 55: Results: Sensitivity to Slow Memory Latency
We vary and of the slow memory
Chart: Slow Memory Latency Multiplier
| x3.0 x3.0 | x4.0 x4.0 | x4.5 x12 | x6.0 x16 | x7.5 x20
ALL | 2.13 | 2.12 | 2.1 | 2.08 | 2.06
FREQ | 3.2 | 3.14 | 2.91 | 2.74 | 2.57
RBLA | 3.33 | 3.27 | 2.99 | 2.86 | 2.79
UH-MEM | 3.6 | 3.45 | 3.39 | 3.23 | 3.15
13%
13%
8%
6%
14%
UH-MEM improves system performance for a wide variety of hybrid memory systems

## Slide 56: More on UH-MEM
Yang Li, Saugata Ghose, Jongmoo Choi, Jin Sun, Hui Wang, and Onur Mutlu, "Utility-Based Hybrid Memory Management" Proceedings of the 19th IEEE Cluster Conference (CLUSTER), Honolulu, Hawaii, USA, September 2017. [Slides (pptx) (pdf)]

## Slide 57: Challenge and Opportunity
Enabling
an Emerging Technology
to Augment DRAM
Managing Hybrid Memories

## Slide 58: Another Challenge
Designing Effective
Large (DRAM) Caches

## Slide 59: One Problem with Large DRAM Caches
A large DRAM cache requires a large metadata (tag + block-based information) store
How do we design an efficient DRAM cache?
DRAM
PCM
CPU
(small, fast cache)
(high capacity)
Mem Ctlr
Mem Ctlr
LOAD X
Access X
Metadata:
X  DRAM
X

## Slide 60: Idea 1: Tags in Memory
Store tags in the same row as data in DRAM
  Store metadata in same row as their data
  Data and metadata can be accessed together
Benefit: No on-chip tag storage overhead
Downsides:
  Cache hit determined only after a DRAM access
  Cache hit requires two DRAM accesses
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 61: Idea 2: Cache Tags in SRAM
Recall Idea 1: Store all metadata in DRAM
  To reduce metadata storage overhead
Idea 2: Cache in on-chip SRAM frequently-accessed metadata
  Cache only a small amount to keep SRAM size small

## Slide 62: Idea 3: Dynamic Data Transfer Granularity
Some applications benefit from caching more data
  They have good spatial locality
Others do not
  Large granularity wastes bandwidth and reduces cache utilization
Idea 3: Simple dynamic caching granularity policy
  Cost-benefit analysis to determine best DRAM cache block size
  Group main memory into sets of rows
  Different sampled row sets follow different fixed caching granularities
  The rest of main memory follows the best granularity
    Cost–benefit analysis: access latency versus number of cachings
    Performed every quantum

## Slide 63
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
TIMBER Performance
-6%
Reduced channel contention and improved spatial locality
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 64
Chart: Normalized Performance per Watt (for Memory System)
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.73082 | 0.75384 | 0.89249 | 1.1769
TIMBER Energy Efficiency
Fewer migrations reduce transmitted data and channel contention
18%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 65: On Large DRAM Cache Design
Justin Meza, Jichuan Chang, HanBin Yoon, Onur Mutlu, and Parthasarathy Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management" IEEE Computer Architecture Letters (CAL), February 2012.

## Slide 66: DRAM Caches: Many Recent Options
Yu+, “Banshee: Bandwidth-Efficient DRAM Caching via Software/Hardware Cooperation,” MICRO 2017.

## Slide 67: Banshee [MICRO 2017]
Tracks presence in cache using TLB and Page Table
  No tag store needed for DRAM cache
  Enabled by a new lightweight lazy TLB coherence protocol
New bandwidth-aware frequency-based replacement policy

## Slide 68: More on Banshee
Xiangyao Yu, Christopher J. Hughes, Nadathur Satish, Onur Mutlu, and Srinivas Devadas, "Banshee: Bandwidth-Efficient DRAM Caching via Software/Hardware Cooperation" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017.

## Slide 69: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 70: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM
Notes: If we look at our system’s today, we have a two-level storage model where memory is directly accessed by ld/st instructions, but storage is accesses by system calls. Disk stores the persistent data, but is slow and can only be accessed as a block. So we transfer data to DRAM, which is fast and byte addressable.

## Slide 71: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM
PCM, STT-RAM
NVM
Non-volatile memories combine characteristics of memory and storage
Notes: However, now we have these emerging non-volatile memories which actually combine the characteristics of both memory and storage. They are fast and byte addressable like DRAM, but also can persist data as storage

## Slide 72: Two-Level Memory/Storage Model
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 73: Unified Memory and Storage with NVM
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 74: PERSISTENT MEMORY
CPU
PERSISTENTMEMORY
Provides an opportunity to manipulate persistent data directly
Ld/St
NVM
Notes: NVM provides an unique opportunity to manipulate persistent data directly in the main memory.

## Slide 75: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 76: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 77: Efficient Data Mapping among Heterogeneous Devices
A persistent memory exposes a large, persistent address space
  But it may use many different devices to satisfy this goal
  From fast, low-capacity volatile DRAM to slow, high-capacity non-volatile HDD or Flash
  And other NVM devices in between
Performance and energy can benefit from good placement of data among these devices
  Utilizing the strengths of each device and avoiding their weaknesses, if possible
  For example, consider two important application characteristics: locality and persistence

## Slide 78: Efficient Data Mapping among Heterogeneous Devices
Notes: Here, we’ve plotted these two important characteristics as axes on a graph. On the bottom is persistence, from temporary – the data does not need to be saved across program executions – on the left to persistent – the data must remain across executions for correct operation – on the right. From bottom to top we have data that has more locality – and is accessed very frequently in a short amount of time or space – to data that has less locality – which may predominantly be accessed in a random manner.
Let’s take a look at two examples of data and how they map onto this space.

## Slide 79: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
Notes: First we have some data that requires high persistence but has little locality. Such data might be the columns in a column store that are only scanned through infrequently. While it is essential that this data remain persistent across runs of the program, it may not be accessed that frequently, and therefore may be more beneficial to place on slightly slower, persistent memory devices, such as Flash.

## Slide 80: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
X
Frequently-updated index for a Content Delivery Network (CDN)  place in DRAM
Applications or system software can provide hints for data placement
Notes: On the other end of the perspective is data that has high locality but is only ephemeral and not needed between executions. Data in a Content Delivery Network that is cached as it is accessed and is constantly being updated and replaced, is a great candidate for placing in DRAM on such systems.

## Slide 81: Evaluated Systems
HDD Baseline
  Traditional system with volatile DRAM memory and persistent HDD storage
  Overheads of operating system and file system code and buffering
NVM Baseline (NB)
  Same as HDD Baseline, but HDD is replaced with NVM
  Still has OS/FS overheads of the two-level storage model
Persistent Memory (PM)
  Uses only NVM (no DRAM) to ensure full-system persistence
  All data accessed using loads and stores
  Does not waste time on system calls
  Data is manipulated directly on the NVM device

## Slide 82: Performance Benefits of a Single-Level Store
~5X
~24X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 83: Energy Benefits of a Single-Level Store
~5X
~16X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 84: On Persistent Memory Benefits & Challenges
Justin Meza, Yixin Luo, Samira Khan, Jishen Zhao, Yuan Xie, and Onur Mutlu, "A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory" Proceedings of the 5th Workshop on Energy-Efficient Design (WEED), Tel-Aviv, Israel, June 2013. Slides (pptx) Slides (pdf)

## Slide 85: Challenge and Opportunity
Combined
Memory & Storage

## Slide 86: Challenge and Opportunity
A Unified Interface to All Data

## Slide 87: One Key Challenge in Persistent Memory
How to ensure consistency of system/data if all memory is persistent?
Two extremes
  Programmer transparent: Let the system handle it
  Programmer only: Let the programmer handle it
Many alternatives in-between…

## Slide 88: CRASH CONSISTENCY PROBLEM
Add a node to a linked list
1. Link to next
2. Link to prev
System crash can result in
inconsistent memory state
Notes: Let’s see an example of crash consistency problem in persistent memory systems. When we add a node in the linked list, there are two operations, first, we need to link the new node to next node and then link the previous node to the new node. Unfortunately due to the write ordering, we cannot guarantee which write will reach the memory first. If there is a power failure, depending on which write persisted, we might have a broken linked list. As a result, after a crash we can have an inconsistent memory state.

## Slide 89: CURRENT SOLUTIONS
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
AtomicBegin {
Insert a new node;
} AtomicEnd;
Limits adoption of NVM
Have to rewrite code with clear partition
between volatile and non-volatile data
Burden on the programmers

## Slide 90: CURRENT SOLUTIONS
void hashtable_update(hashtable_t* ht,
void *key, void *data)
{
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) list_find(chain,
&updatePair);
pair->second = data;
}
Example Code
update a node in a persistent hash table
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
Notes: Current solution propose to use explicit interfaces to protect data from inconsistency.
Let’s see a real code that updates a node in a persistent hash table.

## Slide 91: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Notes: The code looks like this after we use the transactional interface. However, there are several issues in the code.

## Slide 92: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Notes: First, the programmer has to manually declare the persistent object.

## Slide 93: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Need a new implementation
Notes: Second, the programmers need to rewrite the functions so that they correctly manipulate the persistent data

## Slide 94: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Need a new implementation
Third party code
can be inconsistent
Notes: Third, third party code needs to be consistent

## Slide 95: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Need a new implementation
Third party code
can be inconsistent
Prohibited
Operation
Burden on the programmers
Notes: Programmers need to make sure there is no volatile to non-volatile pointers. Clearly writing code for persistent memory is a burden on the general programmers.

## Slide 96: OUR APPROACH: ThyNVM
Goal:
Software transparent consistency in
persistent memory systems
Key Idea:
Periodically checkpoint state;
recover to previous checkpt on crash

## Slide 97: ThyNVM: Summary
Checkpoints at multiple granularities to reduce both checkpointing latency and metadata overhead
Overlaps checkpointing and execution to reduce checkpointing latency
Adapts to DRAM and NVM characteristics
Performs within 4.9% of an idealized DRAM with zero cost consistency
A new hardware-based
checkpointing mechanism

## Slide 98: 2. OVERLAPPING CHECKPOINTING AND EXECUTION
Running
time
Checkpointing
Running
Checkpointing
time
Epoch 0
Epoch 1
Epoch 2
Epoch 0
Epoch 1
Running
Checkpointing
Running
Checkpointing
Running
Checkpointing
Epoch 0
Epoch 1
Notes: Even with the dual granularity checkpointing, checkpointing latency is dominated by the slow DRAM write back. In order to reduce the latency we propose to overlap checkpointing with execution. Instead of stalling when DRAM pages are getting written back to memory, we let the application start the next epoch. This hides the long latency of page writeback scheme.

## Slide 99: More About ThyNVM
Jinglei Ren, Jishen Zhao, Samira Khan, Jongmoo Choi, Yongwei Wu, and Onur Mutlu, "ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems" Proceedings of the 48th International Symposium on Microarchitecture (MICRO), Waikiki, Hawaii, USA, December 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code]

## Slide 100: Another Key Challenge in Persistent Memory
Programming Ease
to Exploit Persistence

## Slide 101: Tools/Libraries to Help Programmers
Himanshu Chauhan, Irina Calciu, Vijay Chidambaram, Eric Schkufza, Onur Mutlu, and Pratap Subrahmanyam, "NVMove: Helping Programmers Move to Byte-Based Persistence" Proceedings of the 4th Workshop on Interactions of NVM/Flash with Operating Systems and Workloads (INFLOW), Savannah, GA, USA, November 2016. [Slides (pptx) (pdf)]

## Slide 102: The Future of Emerging Technologies is Bright
Regardless of challenges
  in underlying technology and overlying problems/requirements
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Can enable:
- Orders of magnitude
improvements
- New applications and
computing systems
Yet, we have to
- Think across the stack
- Design enabling systems

## Slide 103: If In Doubt, Refer to Flash Memory
A very “doubtful” emerging technology
  for at least two decades
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 104: Memory Systems Fundamentals, Recent Research, Challenges, Opportunities Lecture 5: Emerging Memory Technologies
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
9 October 2018
Technion Fast Course 2018