## Slide 1: Memory Systems Fundamentals, Recent Research, Challenges, Opportunities Lecture 7: Interconnects
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
11 October 2018
Technion Fast Course 2018

## Slide 2: Interconnection Networks

## Slide 3: Readings
Required
  Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
Recommended
  Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.

## Slide 4: Interconnection Network Basics

## Slide 5: Where Is Interconnect Used?
To connect components
Many examples
  Processors and processors
  Processors and memories (banks)
  Processors and caches (banks)
  Caches and caches
  I/O devices
Interconnection network

## Slide 6: Why Is It Important?
Affects the scalability of the system
  How large of a system can you build?
  How easily can you add more processors?
Affects performance and energy efficiency
  How fast can processors, caches, and memory communicate?
  How long are the latencies to memory?
  How much energy is spent on communication?

## Slide 7: Interconnection Network Basics
Topology
  Specifies the way switches are wired
  Affects routing, reliability, throughput, latency, building ease
Routing (algorithm)
  How does a message get from source to destination
  Static or adaptive
Buffering and Flow Control
  What do we store within the network?
    Entire packets, parts of packets, etc?
  How do we throttle during oversubscription?
  Tightly coupled with routing strategy

## Slide 8: Terminology
Network interface
  Module that connects endpoints (e.g. processors) to network
  Decouples computation/communication
Link
  Bundle of wires that carry a signal
Switch/router
  Connects fixed number of input channels to fixed number of output channels
Channel
  A single logical connection between routers/switches

## Slide 9: More Terminology
Node
  A router/switch within a network
Message
  Unit of transfer for network’s clients (processors, memory)
Packet
  Unit of transfer for network
Flit
  Flow control digit
  Unit of flow control within network

## Slide 10: Some More Terminology
  Direct or Indirect Networks
  Endpoints sit “inside” (direct) or “outside” (indirect) the network
  E.g. mesh is direct; every node is both endpoint and switch
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
Router (switch), Radix of 2 (2 inputs, 2 outputs)
Abbreviation: Radix-ary
These routers are 2-ary
Indirect
Direct
Notes: What type of network is the one on the right

## Slide 11: Interconnection Network Topology

## Slide 12: Properties of a Topology/Network
Regular or Irregular
  Regular if topology is regular graph (e.g. ring, mesh).
Routing Distance
  number of links/hops along a route
Diameter
  maximum routing distance within the network
Average Distance
  Average number of hops across all valid routes
Notes: Example of irregular network? Internet

## Slide 13: Properties of a Topology/Network
Bisection Bandwidth
  Often used to describe network performance
  Cut network in half and sum bandwidth of links severed
    (Min # channels spanning two halves) * (BW of each channel)
  Meaningful only for recursive topologies
  Can be misleading, because does not account for switch and routing efficiency (and certainly not execution time)
Blocking vs. Non-Blocking
  If connecting any permutation of sources & destinations is possible, network is non-blocking; otherwise network is blocking.
  Rearrangeable non-blocking: Same as non-blocking but might require rearranging connections when switching from one permutation to another.

## Slide 14: Topology
Bus (simplest)
Point-to-point connections (ideal and most costly)
Crossbar (less costly)
Ring
Tree
Omega
Hypercube
Mesh
Torus
Butterfly
…

## Slide 15: Metrics to Evaluate Interconnect Topology
Cost
Latency (in hops, in nanoseconds)
Contention
Many others exist you should think about
  Energy
  Bandwidth
  Overall system performance

## Slide 16: Bus
All nodes connected to a single link
+ Simple + Cost effective for a small number of nodes
+ Easy to implement coherence (snooping and serialization)
- Not scalable to large number of nodes (limited bandwidth, electrical loading  reduced frequency)
- High contention  fast saturation
0
1
2
3
4
5
6
7

## Slide 17: Point-to-Point
Every node connected to every other
with direct/isolated links
+ Lowest contention
+ Potentially lowest latency
+ Ideal, if cost is no issue
-- Highest cost
O(N) connections/ports
per node
O(N2) links
-- Not scalable
-- How to lay out on chip?
0
1
2
3
4
5
6
7

## Slide 18: Crossbar
Every node connected to every other with a shared link for each destination
Enables concurrent transfers to non-conflicting destinations
Could be cost-effective for small number of nodes
+ Low latency and high throughput
- Expensive
- Not scalable  O(N2) cost
- Difficult to arbitrate as N increases
Used in core-to-cache-bank
networks in
- IBM POWER5
- Sun Niagara I/II
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 19: Another Crossbar Design
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 20: Sun UltraSPARC T2 Core-to-Cache Crossbar
High bandwidth interface between 8 cores and 8 L2 banks & NCU
4-stage pipeline: req, arbitration, selection, transmission
2-deep queue for each src/dest pair to hold data transfer request

## Slide 21: Bufferless and Buffered Crossbars
Output
Arbiter
Output
Arbiter
Output
Arbiter
Output
Arbiter
Flow
Control
Flow
Control
Flow
Control
Flow
Control
NI
NI
NI
NI
Buffered
Crossbar
0
1
2
3
NI
NI
NI
NI
Bufferless
Crossbar
0
1
2
3
+ Simpler arbitration/ scheduling
+ Efficient support for variable-size packets
- Requires N2 buffers

## Slide 22: Can We Get Lower Cost than A Crossbar?
Yet still have low contention compared to a bus?
Idea: Multistage networks

## Slide 23: Multistage Logarithmic Networks
Idea: Indirect networks with multiple layers of switches between terminals/nodes
Cost: O(NlogN), Latency: O(logN)
Many variations (Omega, Butterfly, Benes, Banyan, …)
Omega Network:
conflict
Blocking
or
Non-blocking?

## Slide 24: Multistage Networks (Circuit Switched)
A multistage network has more restrictions on feasible concurrent Tx-Rx pairs vs a crossbar
But more scalable than crossbar in cost, e.g., O(N logN) for Butterfly
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 crossbar

## Slide 25: Multistage Networks (Packet Switched)
Packets “hop” from router to router, pending availability of the next-required switch and buffer
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 router

## Slide 26: Aside: Circuit vs. Packet Switching
Circuit switching sets up full path before transmission
  Establish route then send data
  Noone else can use those links while “circuit” is set
  + faster arbitration
  + no buffering
  -- setting up and bringing down “path” takes time
Packet switching routes per packet in each router
  Route each packet individually (possibly via different paths)
  If link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  -- need buffering
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 27: Switching vs. Topology
Circuit/packet switching choice independent of topology
It is a higher-level protocol on how a message gets sent to a destination
However, some topologies are more amenable to circuit vs. packet switching

## Slide 28: Another Example: Delta Network
Single path from source to destination
Each stage has different routers
Proposed to replace costly crossbars as processor-memory interconnect
Janak H. Patel,“Processor-Memory Interconnections for Multiprocessors,” ISCA 1979.
8x8 Delta network

## Slide 29: Another Example: Omega Network
Single path from source to destination
All stages are the same
Used in NYU Ultracomputer
Gottlieb et al. “The NYU Ultracomputer - Designing an MIMD Shared Memory Parallel Computer,” IEEE Trans. On Comp., 1983.

## Slide 30: Combining Operations in the Network
Idea: Combine multiple operations on a shared memory location
Example: Omega network switches combine fetch-and-add operations in NYU Ultracomputer
Fetch-and-add(M, I): return M, replace M with M+I
  Common when parallel processors modify a shared variable, e.g. obtain a chunk of the array
Combining reduces synchronization latency

## Slide 31: Butterfly
Equivalent to Omega Network
Indirect
Used in BBN Butterfly
Conflicts can cause “tree saturation”
  Randomization of route selection helps
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14

## Slide 32: Review: Topologies
Direct
Topology
Crossbar
Mesh
Indirect
Direct/Indirect
Blocking/ Non-blocking
2
1
0
3
2
1
0
3
1
0
3
2
5
4
7
6
1
0
3
2
5
4
7
6
Non-blocking
Blocking
Blocking
Multistage Logarith.
Indirect
Cost
Latency
O(N2)
O(NlogN)
O(N)
O(sqrt(N))
O(1)
O(logN)

## Slide 33: Ring
Each node connected to exactly two other nodes. Nodes form a continuous pathway such that packets can reach any node.
+ Cheap: O(N) cost
- High latency: O(N)
- Not easy to scale
- Bisection bandwidth remains constant
Used in Intel Haswell,
Intel Larrabee, IBM Cell,
many commercial systems today
Notes: KSR machine, Hector

## Slide 34: Unidirectional Ring
Single directional pathway
Simple topology and implementation
  Reasonable performance if N and performance needs (bandwidth & latency) still moderately low
  O(N) cost
  N/2 average hops; latency depends on utilization
R
0
R
1
R
N-2
R
N-1
2
2x2 router

## Slide 35: Bidirectional Rings
Multi-directional pathways, or multiple rings
+ Reduces latency
+ Improves scalability
- Slightly more complex injection policy (need to select which ring to inject a packet into)

## Slide 36: Hierarchical Rings
+ More scalable
+ Lower latency
- More complex

## Slide 37: More on Hierarchical Rings
Ausavarungnirun et al., “Design and Evaluation of Hierarchical Rings with Deflection Routing,” SBAC-PAD 2014.
  http://users.ece.cmu.edu/~omutlu/pub/hierarchical-rings-with-deflection_sbacpad14.pdf
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 38: Mesh
Each node connected to 4 neighbors (N, E, S, W)
O(N) cost
Average latency: O(sqrt(N))
Easy to layout on-chip: regular and equal-length links
Path diversity: many ways to get from one node to another
Used in Tilera 100-core
And many on-chip network
prototypes
Notes: e.g. Tile64

## Slide 39: Torus
Mesh is not symmetric on edges: performance very sensitive to placement of task on edge vs. middle
Torus avoids this problem
+ Higher path diversity (and bisection bandwidth) than mesh
- Higher cost
- Harder to lay out on-chip
- Unequal link lengths

## Slide 40: Torus, continued
Weave nodes to make inter-node latencies ~constant

## Slide 41: Trees
Planar, hierarchical topology
Latency: O(logN)
Good for local traffic
+ Cheap: O(N) cost
+ Easy to Layout
- Root can become a bottleneck
Fat trees avoid this problem (CM-5)
Fat Tree

## Slide 42: CM-5 Fat Tree
Fat tree based on 4x2 switches
Randomized routing on the way up
Combining, multicast, reduction operators supported in hardware
  Thinking Machines Corp., “The Connection Machine CM-5 Technical Summary,” Jan. 1992.

## Slide 43: Hypercube
“N-dimensional cube” or “N-cube”
Latency: O(logN)
Radix: O(logN)
#links: O(NlogN)
+ Low latency
- Hard to lay out in 2D/3D
0000
0101
0100
0001
0011
0010
0110
0111
1000
1101
1100
1001
1011
1010
1110
1111
Notes: Popular in early message-passing computers (e.g., intel iPSC, NCUBE)

## Slide 44: Caltech Cosmic Cube
64-node message passing machine
Seitz, “The Cosmic Cube,” CACM 1985.

## Slide 45: Routing

## Slide 46: Routing Mechanism
Arithmetic
  Simple arithmetic to determine route in regular topologies
  Dimension order routing in meshes/tori
Source Based
  Source specifies output port for each switch in route
  + Simple switches
    no control state: strip output port off header
  - Large header
Table Lookup Based
  Index into table for output port
  + Small header
  - More complex switches
Notes: Any advantages of Table Lookup Based? Easier to support fault tolerance. E.g. can bypass faulty links

## Slide 47: Routing Algorithm
Three Types
  Deterministic: always chooses the same path for a communicating source-destination pair
  Oblivious: chooses different paths, without considering network state
  Adaptive: can choose different paths, adapting to the state of the network
How to adapt
  Local/global feedback
  Minimal or non-minimal paths

## Slide 48: Deterministic Routing
All packets between the same (source, dest) pair take the same path
Dimension-order routing
  First traverse dimension X, then traverse dimension Y
  E.g., XY routing (used in Cray T3D, and many on-chip networks)
+ Simple
+ Deadlock freedom (no cycles in resource allocation)
- Could lead to high contention
- Does not exploit path diversity

## Slide 49: Deadlock
No forward progress
Caused by circular dependencies on resources
Each packet waits for a buffer occupied by another packet downstream

## Slide 50: Handling Deadlock
Avoid cycles in routing
  Dimension order routing
    Cannot build a circular dependency
  Restrict the “turns” each packet can take
Avoid deadlock by adding more buffering (escape paths)
Detect and break deadlock
  Preemption of buffers

## Slide 51: Turn Model to Avoid Deadlock
Idea
  Analyze directions in which packets can turn in the network
  Determine the cycles that such turns can form
  Prohibit just enough turns to break possible cycles
Glass and Ni, “The Turn Model for Adaptive Routing,” ISCA 1992.

## Slide 52: Oblivious Routing: Valiant’s Algorithm
Goal: Balance network load
Idea: Randomly choose an intermediate destination, route to it first, then route from there to destination
  Between source-intermediate and intermediate-dest, can use dimension order routing
+ Randomizes/balances network load
- Non minimal (packet latency can increase)
Optimizations:
  Do this on high load
  Restrict the intermediate node to be close (in the same quadrant)

## Slide 53: Adaptive Routing
Minimal adaptive
  Router uses network state (e.g., downstream buffer occupancy) to pick which “productive” output port to send a packet to
  Productive output port: port that gets the packet closer to its destination
  + Aware of local congestion
  - Minimality restricts achievable link utilization (load balance)
Non-minimal (fully) adaptive
  “Misroute” packets to non-productive output ports based on network state
  + Can achieve better network utilization and load balance
  - Need to guarantee livelock freedom

## Slide 54: More on Adaptive Routing
Can avoid faulty links/routers
Idea: Route around faults
+ Deterministic routing cannot handle faulty components
- Need to change the routing table to disable faulty routes
- Assuming the faulty link/router is detected
One recent example:
Fattah et al., "A Low-Overhead, Fully-Distributed, Guaranteed-Delivery Routing Algorithm for Faulty Network-on-Chips", NOCS 2015.

## Slide 55: Buffering and Flow Control

## Slide 56: Recall: Circuit vs. Packet Switching
Circuit switching sets up full path before transmission
  Establish route then send data
  Noone else can use those links while “circuit” is set
  + faster arbitration
  -- setting up and bringing down “path” takes time
Packet switching routes per packet in each router
  Route each packet individually (possibly via different paths)
  If link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 57: Packet Switched Networks: Packet Format
Header
  routing and control information
Payload
  carries data (non HW specific information)
  can be further divided (framing, protocol stacks…)
Error Code
  generally at tail of packet so it can be generated on the way out
Header
Payload
Error Code

## Slide 58: Handling Contention
Two packets trying to use the same link at the same time
What do you do?
  Buffer one
  Drop one
  Misroute one (deflection)
Tradeoffs?

## Slide 59: Flow Control Methods
Circuit switching
Bufferless (Packet/flit based)
Store and forward (Packet based)
Virtual cut through (Packet based)
Wormhole (Flit based)

## Slide 60: Circuit Switching Revisited
Resource allocation granularity is high
Idea: Pre-allocate resources across multiple switches for a given “flow”
Need to send a probe to set up the path for pre-allocation
+ No need for buffering
+ No contention (flow’s performance is isolated)
+ Can handle arbitrary message sizes
- Lower link utilization: two flows cannot use the same link
- Handshake overhead to set up a “circuit”

## Slide 61: Bufferless Deflection Routing
Destination
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.1
1Baran, “On Distributed Communication Networks.” RAND Tech. Report., 1962 / IEEE Trans.Comm., 1964.
New traffic can be injected
whenever there is a free
output link.

## Slide 62: Bufferless Deflection Routing
Input buffers are eliminated: packets are buffered in pipeline latches and on network links
North
South
East
West
Local
North
South
East
West
Local
Deflection Routing Logic
Input Buffers
  Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.

## Slide 63: Issues In Bufferless Deflection Routing
Livelock
Resulting Router Complexity
Performance & Congestion at High Loads
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "Bufferless and Minimally-Buffered Deflection Routing" Invited Book Chapter in Routing Algorithms in Networks-on-Chip, pp. 241-275, Springer, 2014.

## Slide 64: Store and Forward Flow Control
Packet-based flow control
Store and Forward
  Packet copied entirely into network router before moving to the next node
  Flow control unit is the entire packet
Leads to high per-packet latency
Requires buffering for entire packet in each node
Can we do better?
S
D

## Slide 65: Cut through Flow Control
Another form of packet-based flow control
Start forwarding as soon as header is received and resources (buffer, channel, etc) allocated
  Dramatic reduction in latency
Still allocate buffers and channel bandwidth for full packets
What if packets are large?
S
D

## Slide 66: Cut through Flow Control
What to do if output port is blocked?
Lets the tail continue when the head is blocked, absorbing the whole message into a single switch.
  Requires a buffer large enough to hold the largest packet.
Degenerates to store-and-forward with high contention
Can we do better?

## Slide 67: Wormhole Flow Control
Packets broken into (potentially) smaller flits (buffer/bw allocation unit)
Flits are sent across the fabric in a wormhole fashion
  Body follows head, tail follows body
  Pipelined
  If head blocked, rest of packet stops
  Routing (src/dest) information only in head
How does body/tail know where to go?
Latency almost independent of distance for long messages

## Slide 68: Wormhole Flow Control
Advantages over “store and forward” flow control
  + Lower latency
  + More efficient buffer utilization
Limitations
  - Suffers from head of line blocking
  - If head flit cannot move due to contention, another worm cannot proceed even though links may be idle
1
2
1
2
1
2
Switching Fabric
Input Queues
Outputs
1
2
1
2
HOL Blocking
Idle!

## Slide 69: Head of Line Blocking
A worm can be before another in the router input buffer
Due to FIFO nature, the second worm cannot be scheduled even though it may need to access another output port

## Slide 70: Head of Line Blocking
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds

## Slide 71: Virtual Channel Flow Control
Idea: Multiplex multiple channels over one physical channel
Divide up the input buffer into multiple buffers sharing a single physical channel
Dally, “Virtual Channel Flow Control,” ISCA 1990.

## Slide 72: Virtual Channel Flow Control
Idea: Multiplex multiple channels over one physical channel
Divide up the input buffer into multiple buffers sharing a single physical channel
Dally, “Virtual Channel Flow Control,” ISCA 1990.

## Slide 73: Virtual Channel Flow Control
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 74: A Modern Virtual Channel Based Router

## Slide 75: Other Uses of Virtual Channels
Deadlock avoidance
  Enforcing switching to a different set of virtual channels on some “turns” can break the cyclic dependency of resources
    Enforce order on VCs
  Escape VCs: Have at least one VC that uses deadlock-free routing. Ensure each flit has fair access to that VC.
  Protocol level deadlock: Ensure address and data packets use different VCs  prevent cycles due to intermixing of different packet classes
Prioritization of traffic classes
  Some virtual channels can have higher priority than others

## Slide 76: Review: Flow Control
Store and Forward
S
D
Cut Through / Wormhole
S
D
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds
Shrink Buffers
Reduce latency
Any other issues?
Head-of-Line
Blocking
Use Virtual
Channels

## Slide 77: Review: Flow Control
Store and Forward
S
D
Cut Through / Wormhole
S
D
Shrink Buffers
Reduce latency
Any other issues?
Head-of-Line
Blocking
Use Virtual
Channels
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 78: Communicating Buffer Availability
Credit-based flow control
  Upstream knows how many buffers are downstream
  Downstream passes back credits to upstream
  Significant upstream signaling (esp. for small flits)
On/Off (XON/XOFF) flow control
  Downstream has on/off signal to upstream
Ack/Nack flow control
  Upstream optimistically sends downstream
  Buffer cannot be deallocated until ACK/NACK received
  Inefficiently utilizes buffer space

## Slide 79: Credit-based Flow Control
Round-trip credit delay:
  Time between when buffer empties and when next flit can be processed from that buffer entry
Significant throughput degradation if there are few buffers
Important to size buffers to tolerate credit turn-around
Node 1
Node 2
Flit departs
router
t1
Credit
Process
t2
t3
Credit
Flit
Process
t4
t5
Credit round trip delay

## Slide 80: On/Off (XON/XOFF) Flow Control
Downstream has on/off signal to upstream
Process
Node 1
Node 2
t1
Flit
Flit
Flit
Flit
t2
Foff threshold reached
Off
Flit
Flit
Flit
Flit
Flit
On
Process
Flit
Flit
Flit
Flit
Flit
t3
t4
t5
t6
t7
t8
Foff set to prevent flits arriving before t4 from overflowing
Fon threshold reached
Fon set so that Node 2 does not run out of flits between t5 and t8

## Slide 81: Interconnection Network Performance

## Slide 82: Interconnection Network Performance
Latency
Injection rate into network
Min latency given by topology
Min latency given by routing algorithm
Zero load latency
(topology+routing+ flow control)
Throughput given by topology
Throughput given by routing
Throughput given by flow control

## Slide 83: Ideal Latency
Ideal latency
  Solely due to wire delay between source and destination
  D = Manhattan distance
    The distance between two points measured along axes at right angles.
  v = propagation velocity
  L = packet size
  b = channel bandwidth
Notes: What’s the best we can do?

## Slide 84: Actual Latency
Dedicated wiring impractical
  Long wires segmented with insertion of routers
  D = Manhattan distance
  v = propagation velocity
  L = packet size
  b = channel bandwidth
  H = hops
  Trouter = router latency
  Tc = latency due to contention

## Slide 85: Latency and Throughput Curve
Chart: Injected load (fraction of capacity)
| 0.01 | 0.02 | 0.05 | 0.1 | 0.12 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.60000000000000098 | 0.65000000000000102 | 0.70000000000000095 | 0.750000000000001 | 0.76000000000000101 | 0.85000000000000098 | 0.9 | 0.95000000000000095 | 1
Ideal | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13
On-chip Network | 20 | 20 | 20 | 20 | 20.1 | 20.3 | 20.4 | 20.7 | 21 | 21.6 | 22.5 | 23.8 | 25 | 27 | 29 | 33 | 39 | 50 | 60 | 100 | 100 | 100 | 100

## Slide 86: Network Performance Metrics
Packet latency
Round trip latency
Saturation throughput
Application-level performance: system performance
  Affected by interference among threads/applications

## Slide 87: Buffering and Routing in On-Chip Networks

## Slide 88: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
  Buses and crossbars are not scalable
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Notes: One commonly proposed solution is on-chip network (NoC), which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
is commonly used due to its low layout complexity.
This is also the topology we used for our evaluations, but our mechanism is also applicable to other topologies.
In most multi-core systems, NoC primarily serves cache misses and memory requests.

## Slide 89: On-chip Networks
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Router
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 90: On-Chip vs. Off-Chip Interconnects
On-chip advantages
  Low latency between cores
  No pin constraints
  Rich wiring resources
  Very high bandwidth
  Simpler coordination
On-chip constraints/disadvantages
  2D substrate limits implementable topologies
  Energy/power consumption a key concern
  Complex algorithms undesirable
  Logic area constrains use of wiring resources

## Slide 91: On-Chip vs. Off-Chip Interconnects (II)
Cost
  Off-chip: Channels, pins, connectors, cables
  On-chip: Cost is storage and switches (wires are plentiful)
  Leads to networks with many wide channels, few buffers
Channel characteristics
  On chip short distance  low latency
  On chip RC lines  need repeaters every 1-2mm
    Can put logic in repeaters
Workloads
  Multi-core cache traffic vs. supercomputer interconnect traffic

## Slide 92: On-Chip vs. Off-Chip Tradeoffs
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)

## Slide 93: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Injection Rate
Avg. packet latency
large buffers
medium buffers
small buffers

## Slide 94: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Buffers consume significant energy/power
  Dynamic energy when read/write
  Static energy even when not occupied
Buffers add complexity and latency
  Logic for buffer management
  Virtual channel allocation
  Credit-based flow control
Buffers require significant chip area
  E.g., in TRIPS prototype chip, input buffers occupy 75% of total on-chip network area [Gratz et al, ICCD’06]
Can we get rid of buffers…?

## Slide 95: Going Bufferless…?
How much throughput do we lose?
   How is latency affected?
Up to what injection rates can we use bufferless routing?
 Are there realistic scenarios in which NoC is operated at injection rates below the threshold?
Can we achieve energy reduction?
   If so, how much…?
Can we reduce area, complexity, etc…?
Injection Rate
latency
buffers
no buffers
Answers in our paper!

## Slide 96: BLESS: Bufferless Routing
Always forward all incoming flits to some output port
If no productive direction is available, send to another direction
 packet is deflected
 Hot-potato routing [Baran’64, etc]
Buffered
BLESS
Deflected!

## Slide 97: BLESS: Bufferless Routing
Routing
VC Arbiter
Switch Arbiter
Flit-Ranking
Port-Prioritization
arbitration policy
Flit-Ranking
Create a ranking over all incoming flits
Port-Prioritization
For a given flit in this ranking, find the best free output-port
Apply to each flit in order of ranking

## Slide 98: FLIT-BLESS: Flit-Level Routing
Each flit is routed independently.
Oldest-first arbitration (other policies evaluated in paper)
Network Topology:  Can be applied to most topologies (Mesh, Torus, Hypercube, Trees, …) 1) #output ports ¸ #input ports at every router 2) every router is reachable from every other router
Flow Control & Injection Policy:
   Completely local, inject whenever input port is free
Absence of Deadlocks: every flit is always moving
Absence of Livelocks: with oldest-first ranking
Flit-Ranking
Oldest-first ranking
Port-Prioritization
Assign flit to productive port, if possible. Otherwise, assign to non-productive port.

## Slide 99: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Oldest-first arbitration complex
QoS becomes difficult
Impact on energy…?

## Slide 100: Evaluation – Synthetic Traces
First, the bad news 
Uniform random injection
BLESS has significantly lower saturation throughput compared to buffered baseline.
Chart: Injection Rate (flits per cycle per node)
| 0 | 0.08 | 0.16 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1 | 0.11 | 0.12 | 0.13 | 0.14000000000000001 | 0.15 | 0.16 | 0.17 | 0.18 | 0.19 | 0.2 | 0.21 | 0.22 | 0.23 | 0.24 | 0.25 | 0.26 | 0.27 | 0.28000000000000003 | 0.28999999999999998 | 0.3 | 0.31 | 0.32 | 0.33 | 0.34 | 0.35 | 0.36 | 0.37 | 0.38 | 0.39 | 0.4 | 0.41 | 0.42 | 0.43 | 0.44 | 0.45 | 0.46 | 0.47 | 0.48 | 0.49
FLIT-2 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.3142 | 29.5848 | 29.8829 | 30.2641 | 30.6478 | 31.0371 | 31.5291 | 32.0485 | 32.514 | 33.0424 | 33.6214 | 34.2454 | 34.8647 | 35.5349 | 36.3327 | 37.1874 | 38.0545 | 39.1327 | 40.2686 | 41.8595 | 43.8418 | 48.2112 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-2 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.3889 | 29.6607 | 29.9602 | 30.3294 | 30.7091 | 31.1068 | 31.6101 | 32.1665 | 32.6453 | 33.3123 | 33.9411 | 34.7541 | 35.5301 | 36.508 | 37.6649 | 38.9475 | 40.364 | 42.0965 | 44.2469 | 47.7519 | 57.8451 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
FLIT-1 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.4505 | 22.6682 | 22.8838 | 23.1614 | 23.4459 | 23.7382 | 24.1268 | 24.5155 | 24.8599 | 25.261 | 25.6915 | 26.1454 | 26.6054 | 27.1534 | 27.7909 | 28.4923 | 29.2033 | 30.0413 | 31.1505 | 32.5742 | 34.4702 | 39.8047 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-1 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.585 | 22.8079 | 23.0303 | 23.3201 | 23.6314 | 23.9379 | 24.3375 | 24.7663 | 25.1396 | 25.6411 | 26.1686 | 26.7838 | 27.4439 | 28.2236 | 29.1584 | 30.2441 | 31.4552 | 32.9357 | 35.035 | 38.7007 | 61.9914 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
MIN-AD | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.5388 | 28.6459 | 28.864 | 29.0263 | 29.2029 | 29.4106 | 29.6055 | 29.7855 | 30.0568 | 30.2965 | 30.5566 | 30.8537 | 31.067 | 31.3404 | 31.6329 | 31.9691 | 32.281 | 32.5873 | 33.0224 | 33.3879 | 33.7872 | 34.2208 | 34.6467 | 35.2042 | 35.8494 | 36.3318 | 36.9534 | 37.7887 | 38.4606 | 39.5018 | 40.4692 | 41.6397 | 43.0612 | 44.6159 | 46.6269 | 49.5462 | 54.2782 | 61.2888 | 82.5748 | 101 | 101
BLESS
Best Baseline

## Slide 101: Evaluation – Homogenous Case Study
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1

## Slide 102: Evaluation – Homogenous Case Study
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Observations:
Injection rates not extremely high on average  self-throttling!
For bursts and temporary hotspots, use network links as buffers!

## Slide 103: BLESS Conclusions
For a very wide range of applications and network settings, buffers are not needed in NoC
  Significant energy savings (32% even in dense networks and perfect caches)
  Area-savings of 60%
  Simplified router and network design (flow control, etc…)
  Performance slowdown is minimal (can even increase!)
A strong case for a rethinking of NoC design!
Future research:
  Support for quality of service, different traffic classes, energy-management, etc…

## Slide 104: Bufferless Routing in NoCs
Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  https://users.ece.cmu.edu/~omutlu/pub/bless_isca09.pdf

## Slide 105: Issues In Bufferless Deflection Routing
Livelock
Resulting Router Complexity
Performance & Congestion at High Loads
Quality of Service and Fairness
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "Bufferless and Minimally-Buffered Deflection Routing" Invited Book Chapter in Routing Algorithms in Networks-on-Chip, pp. 241-275, Springer, 2014.

## Slide 106: Low-Complexity Bufferless Routing
Chris Fallin, Chris Craik, and Onur Mutlu, "CHIPPER: A Low-Complexity Bufferless Deflection Router" Proceedings of the 17th International Symposium on High-Performance Computer Architecture (HPCA), pages 144-155, San Antonio, TX, February 2011. Slides (pptx) An extended version as SAFARI Technical Report, TR-SAFARI-2010-001, Carnegie Mellon University, December 2010.

## Slide 107: CHIPPER: A Low-complexity Bufferless Deflection Router
Chris Fallin, Chris Craik, and Onur Mutlu, "CHIPPER: A Low-Complexity Bufferless Deflection Router" Proceedings of the 17th International Symposium on High-Performance Computer Architecture (HPCA), pages 144-155, San Antonio, TX, February 2011. Slides (pptx)

## Slide 108: Motivation
Recent work has proposed bufferless deflection routing (BLESS [Moscibroda, ISCA 2009])
  Energy savings: ~40% in total NoC energy
  Area reduction: ~40% in total NoC area
  Minimal performance loss: ~4% on average
  Unfortunately: unaddressed complexities in router
     long critical path, large reassembly buffers
Goal: obtain these benefits while simplifying the router
in order to make bufferless NoCs practical.
Notes: Router area: see 7.7 in BLESS paper  60.4% * 75% - 18.75% * 25% = 40.6%

## Slide 109: Problems that Bufferless Routers Must Solve
  1. Must provide livelock freedom
   A packet should not be deflected forever
  2. Must reassemble packets upon arrival
Flit: atomic routing unit
0 1 2 3
Packet: one or multiple flits

## Slide 110: A Bufferless Router: A High-Level View
Local Node
Router
Inject
Deflection
Routing
Logic
Crossbar
Reassembly
Buffers
Eject
Problem 2: Packet Reassembly
Problem 1: Livelock Freedom

## Slide 111: Complexity in Bufferless Deflection Routers
  1. Must provide livelock freedom
    Flits are sorted by age, then assigned in age order to output ports
     43% longer critical path than buffered router
  2. Must reassemble packets upon arrival
    Reassembly buffers must be sized for worst case
     4KB per node
    (8x8, 64-byte cache block)

## Slide 112: Problem 1: Livelock Freedom
Inject
Deflection
Routing
Logic
Crossbar
Reassembly
Buffers
Eject
Problem 1: Livelock Freedom

## Slide 113: Livelock Freedom in Previous Work
What stops a flit from deflecting forever?
All flits are timestamped
Oldest flits are assigned their desired ports
Total order among flits
But what is the cost of this?
Flit age forms total order
Guaranteed
progress!
<
<
<
<
<
New traffic is lowest priority

## Slide 114: Age-Based Priorities are Expensive: Sorting
Router must sort flits by age: long-latency sort network
  Three comparator stages for 4 flits
4
1
2
3

## Slide 115: Age-Based Priorities Are Expensive: Allocation
After sorting, flits assigned to output ports in priority order
Port assignment of younger flits depends on that of older flits
  sequential dependence in the port allocator
East?
GRANT: Flit 1  East
DEFLECT: Flit 2  North
GRANT: Flit 3  South
DEFLECT: Flit 4  West
East?
{N,S,W}
{S,W}
{W}
South?
South?
Age-Ordered Flits
1
2
3
4

## Slide 116: Age-Based Priorities Are Expensive
Overall, deflection routing logic based on Oldest-First has a 43% longer critical path than a buffered router
Question: is there a cheaper way to route while guaranteeing livelock-freedom?
Port Allocator
Priority Sort

## Slide 117: Solution: Golden Packet for Livelock Freedom
What is really necessary for livelock freedom?
Key Insight: No total order. it is enough to:
1. Pick one flit to prioritize until arrival
2. Ensure any flit is eventually picked
Flit age forms total order
Guaranteed
progress!
New traffic is
lowest-priority
<
<
<
Guaranteed
progress!
<
“Golden Flit”
partial ordering is sufficient!

## Slide 118: What Does Golden Flit Routing Require?
Only need to properly route the Golden Flit
First Insight: no need for full sort
Second Insight: no need for sequential allocation
Port Allocator
Priority Sort

## Slide 119: Golden Flit Routing With Two Inputs
Let’s route the Golden Flit in a two-input router first
Step 1: pick a “winning” flit: Golden Flit, else random
Step 2: steer the winning flit to its desired output
and deflect other flit
   Golden Flit is always routed toward its destination

## Slide 120: Golden Flit Routing with Four Inputs
Each block makes decisions independently!
  Deflection is a distributed decision
N
E
S
W
N
S
E
W

## Slide 121: Permutation Network Operation
N
E
S
W
wins  swap!
wins  no swap!
wins  no swap!
deflected
Golden:
wins  swap!
x
Port Allocator
Priority Sort
N
E
S
W
N
S
E
W

## Slide 122: Problem 2: Packet Reassembly
Inject/Eject
Reassembly
Buffers
Inject
Eject

## Slide 123: Reassembly Buffers are Large
Worst case: every node sends a packet to one receiver
Why can’t we make reassembly buffers smaller?
Node 0
Node 1
Node N-1
Receiver
one packet in flight
per node
N sending nodes
…
O(N) space!

## Slide 124: Small Reassembly Buffers Cause Deadlock
What happens when reassembly buffer is too small?
Network
cannot eject:
reassembly
buffer full
reassembly
buffer
Many Senders
One Receiver
Remaining flits
must be injected
for forward progress
cannot inject new traffic
network full

## Slide 125: Reserve Space to Avoid Deadlock?
What if every sender asks permission from the receiver before it sends?
 adds additional delay to every request
reassembly buffers
Reserve Slot?
Reserved
ACK
Sender
Reserve Slot
ACK
Send Packet
Receiver

## Slide 126: Escaping Deadlock with Retransmissions
Sender is optimistic instead: assume buffer is free
  If not, receiver drops and NACKs; sender retransmits
   no additional delay in best case
   transmit buffering overhead for all packets
   potentially many retransmits
Reassembly
Buffers
Retransmit
Buffers
NACK!
Sender
ACK
Receiver
Send (2 flits)
Drop, NACK
Other packet completes
Retransmit packet
ACK
Sender frees data

## Slide 127: Solution: Retransmitting Only Once
Key Idea: Retransmit only when space becomes available.
   Receiver drops packet if full; notes which packet it drops
   When space frees up, receiver reserves space so
  retransmit is successful
   Receiver notifies sender to retransmit
Reassembly
Buffers
Retransmit
Buffers
NACK
Sender
Reserved
Receiver
Pending: Node 0 Req 0

## Slide 128: Using MSHRs as Reassembly Buffers
Inject/Eject
Reassembly
Buffers
Inject
Eject
Miss Buffers (MSHRs)
C Using miss buffers for reassembly makes this a
truly bufferless network.

## Slide 129: CHIPPER: Cheap Interconnect Partially-Permuting Router
Inject
Deflection
Routing
Logic
Crossbar
Reassembly
Buffers
Eject
Baseline Bufferless Deflection Router
Large buffers for worst case
Retransmit-Once
Cache miss buffers
Long critical path:
1. Sort by age
2. Allocate ports sequentially
Golden Packet
 Permutation Network

## Slide 130: CHIPPER: Cheap Interconnect Partially-Permuting Router
Inject/Eject
Miss Buffers (MSHRs)
Inject
Eject

## Slide 131: EVALUATION

## Slide 132: Methodology
Multiprogrammed workloads: CPU2006, server, desktop
  8x8 (64 cores), 39 homogeneous and 10 mixed sets
Multithreaded workloads: SPLASH-2, 16 threads
  4x4 (16 cores), 5 applications
System configuration
  Buffered baseline: 2-cycle router, 4 VCs/channel, 8 flits/VC
  Bufferless baseline: 2-cycle latency, FLIT-BLESS
  Instruction-trace driven, closed-loop, 128-entry OoO window
  64KB L1, perfect L2 (stresses interconnect), XOR mapping

## Slide 133: Methodology
Hardware modeling
  Verilog models for CHIPPER, BLESS, buffered logic
    Synthesized with commercial 65nm library
  ORION for crossbar, buffers and links
Power
  Static and dynamic power from hardware models
  Based on event counts in cycle-accurate simulations

## Slide 134: Results: Performance Degradation
Chart: Multithreaded
| luc | cholesky | radix | fft | lun | AVG
Buffered | 1 | 1 | 1 | 1 | 1 | 1
BLESS | 1.0029 | 1.0018 | 0.98947 | 0.98772 | 1.0053 | 0.99744
CHIPPER | 1.0018 | 1.0012 | 0.97236 | 0.96885 | 0.96259 | 0.98136
Chart: Multiprogrammed (subset of 49 total)
| perlbench | tonto | gcc | h264ref | vpr | search.1 | MIX.5 | MIX.2 | MIX.8 | MIX.0 | MIX.6 | GemsFDTD | stream | mcf | AVG (full set)
Buffered | 63.9797 | 63.6791 | 63.5732 | 63.3609 | 61.1795 | 60.5003 | 60.4737 | 60.2887 | 57.7855 | 57.6859 | 57.4864 | 48.0577 | 41.9916 | 22.5714 | 55.5307
BLESS | 63.9892 | 63.8161 | 63.7649 | 63.649 | 61.6634 | 60.0978 | 60.0345 | 60.1977 | 56.4544 | 56.4568 | 56.6327 | 43.5859 | 31.6 | 15.4656 | 53.4814
CHIPPER | 63.9875 | 63.7929 | 63.7101 | 63.5642 | 57.5277 | 54.6854 | 56.5988 | 57.3718 | 50.003 | 51.7054 | 51.2283 | 33.0817 | 22.1335 | 11.3238 | 49.5151
13.6%
1.8%
3.6%
49.8%
C Minimal loss for low-to-medium-intensity workloads

## Slide 135: Results: Power Reduction
Chart: Multiprogrammed (subset of 49 total)
| perlbench | tonto | gcc | h264ref | vpr | search.1 | MIX.5 | MIX.2 | MIX.8 | MIX.0 | MIX.6 | GemsFDTD | stream | mcf | AVG (full set)
Buffered | 5.8772 | 6.2615 | 6.3198 | 6.475 | 9.5689 | 10.1378 | 10.0346 | 9.6586 | 10.9838 | 11.0939 | 11.07 | 12.8089 | 14.8531 | 15.3401 | 9.8883
BLESS | 1.1599 | 1.444 | 1.4834 | 1.6039 | 4.2738 | 5.3655 | 5.2363 | 4.8336 | 6.7843 | 6.7853 | 6.6748 | 9.04 | 10.3725 | 10.7364 | 5.275
CHIPPER | 0.94114 | 1.2232 | 1.2651 | 1.3849 | 4.1573 | 5.3494 | 4.622 | 4.3107 | 6.1701 | 6.2371 | 6.0794 | 8.0081 | 9.9745 | 10.209 | 4.924
Chart: Multithreaded
| luc | cholesky | radix | fft | lun | AVG
Buffered | 1.5231 | 1.4974 | 1.652 | 1.6945 | 2.0545 | 1.6843
BLESS | 0.33073 | 0.31291 | 0.51824 | 0.55499 | 0.81791 | 0.50696
CHIPPER | 0.27643 | 0.25857 | 0.47897 | 0.52078 | 0.77466 | 0.46188
54.9%
73.4%
C Removing buffers  majority of power savings
C Slight savings from BLESS to CHIPPER

## Slide 136: Results: Area and Critical Path Reduction
Chart: Normalized Router Area
| Buffered | BLESS | CHIPPER
Area | 1 | 0.6478 | 0.63761
Chart: Normalized Critical Path
| Buffered | BLESS | CHIPPER
Critical Path | 1 | 1.4255 | 1.0106
-36.2%
-29.1%
+1.1%
-1.6%
C CHIPPER maintains area savings of BLESS
C Critical path becomes competitive to buffered

## Slide 137: Conclusions
Two key issues in bufferless deflection routing
  livelock freedom and packet reassembly
Bufferless deflection routers were high-complexity and impractical
  Oldest-first prioritization  long critical path in router
  No end-to-end flow control for reassembly  prone to deadlock with reasonably-sized reassembly buffers
CHIPPER is a new, practical bufferless deflection router
  Golden packet prioritization  short critical path in router
  Retransmit-once protocol  deadlock-free packet reassembly
  Cache miss buffers as reassembly buffers  truly bufferless network
CHIPPER frequency comparable to buffered routers at much lower area and power cost, and minimal performance loss

## Slide 138: More on CHIPPER
Chris Fallin, Chris Craik, and Onur Mutlu, "CHIPPER: A Low-Complexity Bufferless Deflection Router" Proceedings of the 17th International Symposium on High-Performance Computer Architecture (HPCA), pages 144-155, San Antonio, TX, February 2011. Slides (pptx) An extended version as SAFARI Technical Report, TR-SAFARI-2010-001, Carnegie Mellon University, December 2010.

## Slide 139: Minimally-Buffered Deflection Routing
Bufferless deflection routing offers reduced power & area
But, high deflection rate hurts performance at high load
MinBD (Minimally-Buffered Deflection Router) introduces:
  Side buffer to hold only flits that would have been deflected
  Dual-width ejection to address ejection bottleneck
  Two-level prioritization to avoid unnecessary deflections
MinBD yields reduced power (31%) & reduced area (36%) relative to buffered routers
MinBD yields improved performance (8.1% at high load) relative to bufferless routers  closes half of perf. gap
MinBD has the best energy efficiency of all evaluated designs with competitive performance

## Slide 140: Minimally-Buffered Deflection Routing
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect" Proceedings of the 6th ACM/IEEE International Symposium on Networks on Chip (NOCS), Lyngby, Denmark, May 2012. Slides (pptx) (pdf)

## Slide 141: “Bufferless” Hierarchical Rings
Ausavarungnirun et al., “Design and Evaluation of Hierarchical Rings with Deflection Routing,” SBAC-PAD 2014.
  http://users.ece.cmu.edu/~omutlu/pub/hierarchical-rings-with-deflection_sbacpad14.pdf
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 142: “Bufferless” Hierarchical Rings (II)
Rachata Ausavarungnirun, Chris Fallin, Xiangyao Yu, Kevin Chang, Greg Nazario, Reetuparna Das, Gabriel Loh, and Onur Mutlu, "A Case for Hierarchical Rings with Deflection Routing: An Energy-Efficient On-Chip Communication Substrate" Parallel Computing (PARCO), to appear in 2016.
  arXiv.org version, February 2016.

## Slide 143: Summary of Six Years of Research
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "Bufferless and Minimally-Buffered Deflection Routing" Invited Book Chapter in Routing Algorithms in Networks-on-Chip, pp. 241-275, Springer, 2014.

## Slide 144: More Readings
Studies of congestion and congestion control in on-chip vs. internet-like networks
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)
George Nychis, Chris Fallin, Thomas Moscibroda, and Onur Mutlu, "Next Generation On-Chip Networks: What Kind of Congestion Control Do We Need?" Proceedings of the 9th ACM Workshop on Hot Topics in Networks (HOTNETS), Monterey, CA, October 2010. Slides (ppt) (key)

## Slide 145: On-Chip vs. Off-Chip Tradeoffs
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)

## Slide 146: HAT: Heterogeneous Adaptive Throttling for On-Chip Networks
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)
Notes: Name: … phd student from CMU
Ttitle
collaborative work done with rachata, chris, and Dr. Onur Mutlu

## Slide 147: Executive Summary
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing performance
Observations:
1) Some applications are more sensitive to network latency than others 2) Applications must be throttled differently to achieve peak performance
Key Idea: Heterogeneous Adaptive Throttling (HAT) 1) Application-aware source throttling 2) Network-load-aware throttling rate adjustment
Result: Improves performance and energy efficiency over state-of-the-art source throttling policies
Notes: Here is a one slide summary of what I’ll present today
One major problems is that packets … which causes congestion. As a result, this reduces system performance due to increased network latency.
We make two key observations in this work:
First, some apps are more sen to network latency than others
Second, apps ……
Based on these two key observations, we develop a new source throttling mechanism called HAT to mitigate the detrimental effect of congestion.
It has two key components:
First, HAT performs app-aware source throttling, which selectively throttles certain applications.
Second, BLUE, which dynamically adjusts throttling rate to achieve high perf
Our evaluation shows that HAT improves perf…..

## Slide 148: Throttling Based Fairness in NoCs
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)

## Slide 149: Packet Scheduling

## Slide 150: Packet Scheduling
Which packet to choose for a given output port?
  Router needs to prioritize between competing flits
  Which input port?
  Which virtual channel?
  Which application’s packet?
Common strategies
  Round robin across virtual channels
  Oldest packet first (or an approximation)
  Prioritize some virtual channels over others
Better policies in a multi-core environment
  Use application characteristics

## Slide 151: Application-Aware Packet Scheduling
  Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.

## Slide 152: The Problem: Packet Scheduling
Network-on-Chip
L2$
L2$
L2$
L2$
Bank
mem cont
Memory Controller
P
Accelerator
L2$
Bank
L2$
Bank
P
P
P
P
P
P
P
Network-on-Chip
Network-on-Chip is a critical resource
shared by multiple applications
App1
App2
App N
App N-1

## Slide 153: The Problem: Packet Scheduling
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Routers
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 154: The Problem: Packet Scheduling
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE

## Slide 155: The Problem: Packet Scheduling
Conceptual
View
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
VC
1
VC
2
From East
From West
From North
From South
From PE
Allocator
(SA)

## Slide 156
Scheduler
Conceptual
View
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
Which packet to choose?
The Problem: Packet Scheduling

## Slide 157: The Problem: Packet Scheduling
Existing scheduling policies
  Round Robin
  Age
Problem 1: Local to a router
  Lead to contradictory decision making between routers: packets from one application may be prioritized at one router, to be delayed at next.
Problem 2: Application oblivious
  Treat all applications packets equally
  But applications are heterogeneous
Solution : Application-aware global scheduling policies.

## Slide 158: STC Scheduling Example
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 0
Packet Injection Order at Processor
Core1 Core2 Core3
Batching interval length = 3 cycles
Ranking order =
Batch 1
Batch 2

## Slide 159: STC Scheduling Example
4
8
5
1
7
2
1
6
2
1
3
Router
Scheduler
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 2
Batch 1
Batch 0
Applications

## Slide 160: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
3
2
8
7
6
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age |  |  |  | 
STC |  |  |  | 
Time

## Slide 161: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
3
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC |  |  |  | 
Time
Time

## Slide 162: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
2
3
3
5
4
6
7
8
1
2
2
STC
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC | 1 | 3 | 11 | 5.0
Ranking order
Time
Time
Time

## Slide 163: Application-Aware Prioritization in NoCs
Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.
  https://users.ece.cmu.edu/~omutlu/pub/app-aware-noc_micro09.pdf

## Slide 164: Slack-Based Packet Scheduling
Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Aergia: Exploiting Packet Latency Slack in On-Chip Networks" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 106-116, Saint-Malo, France, June 2010. Slides (pptx)

## Slide 165: Low-Cost QoS in On-Chip Networks (I)
Boris Grot, Stephen W. Keckler, and Onur Mutlu, "Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip" Proceedings of the 42nd International Symposium on Microarchitecture (MICRO), pages 268-279, New York, NY, December 2009. Slides (pdf)

## Slide 166: Low-Cost QoS in On-Chip Networks (II)
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees" Proceedings of the 38th International Symposium on Computer Architecture (ISCA), San Jose, CA, June 2011. Slides (pptx)

## Slide 167: Interconnect Readings

## Slide 168: Application-Aware Prioritization in NoCs
Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.
  https://users.ece.cmu.edu/~omutlu/pub/app-aware-noc_micro09.pdf

## Slide 169: Slack-Based Packet Scheduling
Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Aergia: Exploiting Packet Latency Slack in On-Chip Networks" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 106-116, Saint-Malo, France, June 2010. Slides (pptx)

## Slide 170: Low-Cost QoS in On-Chip Networks (I)
Boris Grot, Stephen W. Keckler, and Onur Mutlu, "Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip" Proceedings of the 42nd International Symposium on Microarchitecture (MICRO), pages 268-279, New York, NY, December 2009. Slides (pdf)

## Slide 171: Low-Cost QoS in On-Chip Networks (II)
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees" Proceedings of the 38th International Symposium on Computer Architecture (ISCA), San Jose, CA, June 2011. Slides (pptx)

## Slide 172: Throttling Based Fairness in NoCs
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)

## Slide 173: Scalability: Express Cube Topologies
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Express Cube Topologies for On-Chip Interconnects" Proceedings of the 15th International Symposium on High-Performance Computer Architecture (HPCA), pages 163-174, Raleigh, NC, February 2009. Slides (ppt)

## Slide 174: Scalability: Slim NoC
Maciej Besta, Syed Minhaj Hassan, Sudhakar Yalamanchili, Rachata Ausavarungnirun, Onur Mutlu, Torsten Hoefler, "Slim NoC: A Low-Diameter On-Chip Network Topology for High Energy Efficiency and Scalability" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pdf)]

## Slide 175: Bufferless Routing in NoCs
Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  https://users.ece.cmu.edu/~omutlu/pub/bless_isca09.pdf

## Slide 176: CHIPPER: Low-Complexity Bufferless
Chris Fallin, Chris Craik, and Onur Mutlu, "CHIPPER: A Low-Complexity Bufferless Deflection Router" Proceedings of the 17th International Symposium on High-Performance Computer Architecture (HPCA), pages 144-155, San Antonio, TX, February 2011. Slides (pptx) An extended version as SAFARI Technical Report, TR-SAFARI-2010-001, Carnegie Mellon University, December 2010.

## Slide 177: Minimally-Buffered Deflection Routing
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect" Proceedings of the 6th ACM/IEEE International Symposium on Networks on Chip (NOCS), Lyngby, Denmark, May 2012. Slides (pptx) (pdf)

## Slide 178: “Bufferless” Hierarchical Rings
Ausavarungnirun et al., “Design and Evaluation of Hierarchical Rings with Deflection Routing,” SBAC-PAD 2014.
  http://users.ece.cmu.edu/~omutlu/pub/hierarchical-rings-with-deflection_sbacpad14.pdf
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 179: “Bufferless” Hierarchical Rings (II)
Rachata Ausavarungnirun, Chris Fallin, Xiangyao Yu, Kevin Chang, Greg Nazario, Reetuparna Das, Gabriel Loh, and Onur Mutlu, "A Case for Hierarchical Rings with Deflection Routing: An Energy-Efficient On-Chip Communication Substrate" Parallel Computing (PARCO), to appear in 2016.
  arXiv.org version, February 2016.

## Slide 180: Summary of Six Years of Research
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "Bufferless and Minimally-Buffered Deflection Routing" Invited Book Chapter in Routing Algorithms in Networks-on-Chip, pp. 241-275, Springer, 2014.

## Slide 181: On-Chip vs. Off-Chip Tradeoffs
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)

## Slide 182: Slowdown Estimation in NoCs
Xiyue Xiang, Saugata Ghose, Onur Mutlu, and Nian-Feng Tzeng, "A Model for Application Slowdown Estimation in On-Chip Networks and Its Use for Improving System Fairness and Performance" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016. [Slides (pptx) (pdf)]

## Slide 183: Handling Multicast and Hotspot Issues
Xiyue Xiang, Wentao Shi, Saugata Ghose, Lu Peng, Onur Mutlu, and Nian-Feng Tzeng, "Carpool: A Bufferless On-Chip Network Supporting Adaptive Multicast and Hotspot Alleviation" Proceedings of the International Conference on Supercomputing (ICS), Chicago, IL, USA, June 2017. [Slides (pptx) (pdf)]

## Slide 184: Memory Systems Fundamentals, Recent Research, Challenges, Opportunities Lecture 7: Interconnects
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
11 October 2018
Technion Fast Course 2018

## Slide 185: MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect" Proceedings of the 6th ACM/IEEE International Symposium on Networks on Chip (NOCS), Lyngby, Denmark, May 2012. Slides (pptx) (pdf)

## Slide 186: Bufferless Deflection Routing
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.
Removing buffers yields significant benefits
  Reduces power (CHIPPER: reduces NoC power by 55%)
  Reduces die area (CHIPPER: reduces NoC area by 36%)
But, at high network utilization (load), bufferless deflection routing causes unnecessary link & router traversals
  Reduces network throughput and application performance
  Increases dynamic power
Goal: Improve high-load performance of low-cost deflection networks by reducing the deflection rate.

## Slide 187: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 188: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 189: Issues in Bufferless Deflection Routing
Correctness: Deliver all packets without livelock
  CHIPPER1: Golden Packet
  Globally prioritize one packet until delivered
Correctness: Reassemble packets without deadlock
  CHIPPER1: Retransmit-Once
Performance: Avoid performance degradation at high load
  MinBD
1 Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.

## Slide 190: Key Performance Issues
1. Link contention: no buffers to hold traffic  any link contention causes a deflection
 use side buffers
2. Ejection bottleneck: only one flit can eject per router per cycle  simultaneous arrival causes deflection
 eject up to 2 flits/cycle
3. Deflection arbitration: practical (fast) deflection arbiters deflect unnecessarily
 new priority scheme (silver flit)

## Slide 191: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 192: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 193: Addressing Link Contention
Problem 1: Any link contention causes a deflection
Buffering a flit can avoid deflection on contention
But, input buffers are expensive:
  All flits are buffered on every hop  high dynamic energy
  Large buffers necessary  high static energy and large area
Key Idea 1: add a small buffer to a bufferless deflection router to buffer only flits that would have been deflected

## Slide 194: How to Buffer Deflected Flits
Baseline Router
Eject
Inject
1 Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.
Destination
Destination
DEFLECTED

## Slide 195: How to Buffer Deflected Flits
Side-Buffered Router
Eject
Inject
Step 1. Remove up to one deflected flit per cycle from the outputs.
Step 2. Buffer this flit in a small FIFO “side buffer.”
Step 3. Re-inject this flit into pipeline when a slot is available.
Side Buffer
Destination
Destination
DEFLECTED

## Slide 196: Why Could A Side Buffer Work Well?
Buffer some flits and deflect other flits at per-flit level
  Relative to bufferless routers, deflection rate reduces (need not deflect all contending flits)
   4-flit buffer reduces deflection rate by 39%
  Relative to buffered routers, buffer is more efficiently used (need not buffer all flits)
     similar performance with 25% of buffer space

## Slide 197: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 198: Addressing the Ejection Bottleneck
Problem 2: Flits deflect unnecessarily because only one flit can eject per router per cycle
In 20% of all ejections, ≥ 2 flits could have ejected  all but one flit must deflect and try again
 these deflected flits cause additional contention
Ejection width of 2 flits/cycle reduces deflection rate 21%
Key idea 2: Reduce deflections due to a single-flit ejection port by allowing two flits to eject per cycle

## Slide 199: Addressing the Ejection Bottleneck
Single-Width Ejection
Eject
Inject
DEFLECTED

## Slide 200: Addressing the Ejection Bottleneck
Dual-Width Ejection
Eject
Inject
For fair comparison, baseline routers have dual-width ejection for perf. (not power/area)

## Slide 201: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 202: Improving Deflection Arbitration
Problem 3: Deflections occur unnecessarily because fast arbiters must use simple priority schemes
Age-based priorities (several past works): full priority order gives fewer deflections, but requires slow arbiters
State-of-the-art deflection arbitration (Golden Packet & two-stage permutation network)
  Prioritize one packet globally (ensure forward progress)
  Arbitrate other flits randomly (fast critical path)
Random common case leads to uncoordinated arbitration

## Slide 203: Fast Deflection Routing Implementation
Let’s route in a two-input router first:
Step 1: pick a “winning” flit (Golden Packet, else random)
Step 2: steer the winning flit to its desired output
and deflect other flit
   Highest-priority flit always routes to destination

## Slide 204: Fast Deflection Routing with Four Inputs
Each block makes decisions independently
  Deflection is a distributed decision
N
E
S
W
N
S
E
W

## Slide 205: Unnecessary Deflections in Fast Arbiters
How does lack of coordination cause unnecessary deflections?
  1. No flit is golden (pseudorandom arbitration)
  2. Red flit wins at first stage
  3. Green flit loses at first stage (must be deflected now)
  4. Red flit loses at second stage; Red and Green are deflected
Destination
Destination
all flits have
equal priority
unnecessary
deflection!

## Slide 206: Improving Deflection Arbitration
Key idea 3: Add a priority level and prioritize one flit to ensure at least one flit is not deflected in each cycle
Highest priority: one Golden Packet in network
  Chosen in static round-robin schedule
  Ensures correctness
Next-highest priority: one silver flit per router per cycle
  Chosen pseudo-randomly & local to one router
  Enhances performance

## Slide 207: Adding A Silver Flit
Randomly picking a silver flit ensures one flit is not deflected
  1. No flit is golden but Red flit is silver
  2. Red flit wins at first stage (silver)
  3. Green flit is deflected at first stage
  4. Red flit wins at second stage (silver); not deflected
Destination
Destination
At least one flit
is not deflected
red flit has
higher priority
all flits have
equal priority

## Slide 208: Minimally-Buffered Deflection Router
Eject
Inject
Problem 1: Link Contention
Solution 1: Side Buffer
Problem 2: Ejection Bottleneck
Solution 2: Dual-Width Ejection
Problem 3: Unnecessary Deflections
Solution 3: Two-level priority scheme

## Slide 209: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration

## Slide 210: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 211: Methodology: Simulated System
Chip Multiprocessor Simulation
  64-core and 16-core models
  Closed-loop core/cache/NoC cycle-level model
  Directory cache coherence protocol (SGI Origin-based)
  64KB L1, perfect L2 (stresses interconnect), XOR-mapping
  Performance metric: Weighted Speedup (similar conclusions from network-level latency)
  Workloads: multiprogrammed SPEC CPU2006
    75 randomly-chosen workloads
    Binned into network-load categories by average injection rate

## Slide 212: Methodology: Routers and Network
Input-buffered virtual-channel router
  8 VCs, 8 flits/VC [Buffered(8,8)]: large buffered router
  4 VCs, 4 flits/VC [Buffered(4,4)]: typical buffered router
  4 VCs, 1 flit/VC [Buffered(4,1)]: smallest deadlock-free router
  All power-of-2 buffer sizes up to (8, 8) for perf/power sweep
Bufferless deflection router: CHIPPER1
Bufferless-buffered hybrid router: AFC2
  Has input buffers and deflection routing logic
  Performs coarse-grained (multi-cycle) mode switching
Common parameters
  2-cycle router latency, 1-cycle link latency
  2D-mesh topology (16-node: 4x4; 64-node: 8x8)
  Dual ejection assumed for baseline routers (for perf. only)
1Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.
2Jafri et al., “Adaptive Flow Control for Robust Performance and Energy”, MICRO 2010.

## Slide 213: Methodology: Power, Die Area, Crit. Path
Hardware modeling
  Verilog models for CHIPPER, MinBD, buffered control logic
    Synthesized with commercial 65nm library
  ORION 2.0 for datapath: crossbar, muxes, buffers and links
Power
  Static and dynamic power from hardware models
  Based on event counts in cycle-accurate simulations
  Broken down into buffer, link, other

## Slide 214: Reduced Deflections & Improved Perf.
Deflection
Chart: Weighted Speedup
| AVG
Baseline | 13.3104
B (Side-Buf) | 12.7312
D (Dual-Eject) | 13.8075
S (Silver Flits) | 13.402
B+D | 14.0867
B+S+D (MinBD) | 14.1847
Rate
28%
17%
22%
27%
11%
10%
All mechanisms individually reduce deflections
2. Side buffer alone is not sufficient for performance (ejection bottleneck remains)
3. Overall, 5.8% over baseline, 2.7% over dual-eject by reducing deflections 64% / 54%
5.8%
2.7%

## Slide 215: Overall Performance Results
Chart: Injection Rate
| 0.0 - 0.15 | 0.15 - 0.30 | 0.30 - 0.40 | 0.40 - 0.50 | > 0.50 | AVG
Buffered (8,8) | 16.0051 | 15.8617 | 15.1919 | 14.2118 | 11.8768 | 14.6295
Buffered (4,4) | 16.0049 | 15.8602 | 15.1612 | 14.1471 | 11.7073 | 14.5761
Buffered (4,1) | 15.9983 | 15.8027 | 14.8748 | 13.5043 | 10.4798 | 14.132
CHIPPER | 15.9451 | 15.4841 | 14.5144 | 13.1601 | 9.9339 | 13.8075
AFC (4,4) | 15.9907 | 15.8249 | 15.1374 | 14.1132 | 10.872 | 14.3876
MinBD-4 | 15.919 | 15.5898 | 14.893 | 13.7518 | 10.7399 | 14.1787
Improves 2.7% over CHIPPER (8.1% at high load)
Similar perf. to Buffered (4,1) @ 25% of buffering space
2.7%
8.1%
2.7%
8.3%
Within 2.7% of Buffered (4,4) (8.3% at high load)

## Slide 216: Overall Power Results
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
static | 1.6291 | 1.047 | 0.74594 | 0.52767 | 0.86902 | 0.55326
dynamic | 0.92052 | 0.79869 | 0.70841 | 0.92607 | 0.84745 | 0.70553
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
buffer | 1.0994 | 0.40037 | 0.04931 | 0 | 0.24432 | 0.023553
non-buffer | 1.4502 | 1.4453 | 1.405 | 1.4537 | 1.4721 | 1.2352
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
static buffer | 0.91433 | 0.3323 | 0.031218 | 0 | 0.13325 | 0.020768
static link | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115
static other | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099
dynamic buffer | 0.18502 | 0.068074 | 0.018092 | 0 | 0.11107 | 0.0027846
dynamic link | 0.59769 | 0.59372 | 0.56097 | 0.71132 | 0.59769 | 0.53927
dynamic other | 0.13782 | 0.1369 | 0.12935 | 0.21475 | 0.13869 | 0.16348
Buffers are significant fraction of power in baseline routers
Buffer power is much smaller in MinBD (4-flit buffer)
Dynamic power increases with deflection routing
Dynamic power reduces in MinBD relative to CHIPPER

## Slide 217: Performance-Power Spectrum
Chart: Network Power (W)
| 2.5495840000000012 | 2.2484410000000001 | 2.0851260000000011 | 1.522975 | 2.0001210000000058 | 1.8457140000000001 | 1.753193 | 1.4543509999999999 | 1.723579 | 1.6376170000000001 | 1.5749899999999999 | 1.401160999999997 | 1.5788709999999999 | 1.463406 | 1.520311 | 1.3443639999999999
 | 14.6295 | 14.612 | 14.5288 | 14.3117 | 14.6259 | 14.5761 | 14.4304 | 14.132 | 14.6045 | 14.4883 | 14.247 | 13.8303 | 14.523 | 13.9062 | 14.304 | 13.3269
 | 14.3876
 | 13.8075
 | 14.1787
Most energy-efficient (perf/watt) of any evaluated network router design
Buf (4,4)
Buf (4,1)
More Perf/Power
Less Perf/Power
Buf (8,8)
AFC
CHIPPER
MinBD

## Slide 218: Die Area and Critical Path
Chart: Normalized Die Area
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | MinBD
Area | 2.06 | 1.69 | 1.6 | 1 | 1.03
Chart: Normalized Critical Path
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | MinBD
Critical Path | 0.99 | 0.99 | 0.99 | 1 | 1.07
Only 3% area increase over CHIPPER (4-flit buffer)
Reduces area by 36% from Buffered (4,4)
Increases by 7% over CHIPPER, 8% over Buffered (4,4)
+3%
-36%
+7%
+8%

## Slide 219: Conclusions
Bufferless deflection routing offers reduced power & area
But, high deflection rate hurts performance at high load
MinBD (Minimally-Buffered Deflection Router) introduces:
  Side buffer to hold only flits that would have been deflected
  Dual-width ejection to address ejection bottleneck
  Two-level prioritization to avoid unnecessary deflections
MinBD yields reduced power (31%) & reduced area (36%) relative to buffered routers
MinBD yields improved performance (8.1% at high load) relative to bufferless routers  closes half of perf. gap
MinBD has the best energy efficiency of all evaluated designs with competitive performance

## Slide 220: Minimally-Buffered Deflection Routing
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect" Proceedings of the 6th ACM/IEEE International Symposium on Networks on Chip (NOCS), Lyngby, Denmark, May 2012. Slides (pptx) (pdf)

## Slide 221: More Readings
Studies of congestion and congestion control in on-chip vs. internet-like networks
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)
George Nychis, Chris Fallin, Thomas Moscibroda, and Onur Mutlu, "Next Generation On-Chip Networks: What Kind of Congestion Control Do We Need?" Proceedings of the 9th ACM Workshop on Hot Topics in Networks (HOTNETS), Monterey, CA, October 2010. Slides (ppt) (key)

## Slide 222: HAT: Heterogeneous Adaptive Throttling for On-Chip Networks
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)
Notes: Name: … phd student from CMU
Ttitle
collaborative work done with rachata, chris, and Dr. Onur Mutlu

## Slide 223: Executive Summary
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing performance
Observations:
1) Some applications are more sensitive to network latency than others 2) Applications must be throttled differently to achieve peak performance
Key Idea: Heterogeneous Adaptive Throttling (HAT) 1) Application-aware source throttling 2) Network-load-aware throttling rate adjustment
Result: Improves performance and energy efficiency over state-of-the-art source throttling policies
Notes: Here is a one slide summary of what I’ll present today
One major problems is that packets … which causes congestion. As a result, this reduces system performance due to increased network latency.
We make two key observations in this work:
First, some apps are more sen to network latency than others
Second, apps ……
Based on these two key observations, we develop a new source throttling mechanism called HAT to mitigate the detrimental effect of congestion.
It has two key components:
First, HAT performs app-aware source throttling, which selectively throttles certain applications.
Second, BLUE, which dynamically adjusts throttling rate to achieve high perf
Our evaluation shows that HAT improves perf…..

## Slide 224: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: Here is the outline for the talk.
I’ve briefly talked about some background on nocs.
Next I’ll talk about the motivation and key idea of our work.

## Slide 225: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Router designs
  Buffered: Input buffers to hold contending packets
  Bufferless: Misroute (deflect) contending packets
Notes: In multi-core processors, interconnect serves as a communication substrate for cores, caches, ….
However as core count continues to increase, conventional interconnects such as busses and crossbards no longer scale adequately.
The commonly proposed solution is on-chip network, which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
Is commonly used due to its low layout complexity.
In most multi-core systems, NoC primarily serves cache misses and memory requests.
A conventional router design for an on-chip network often have input buffers to hold ….
Alternatively, some other router designs have proposed eliminating these buffers and instead deflect contending packets to different links.

## Slide 226: Network Congestion Reduces Performance
Network congestion:
Network throughput
Application performance
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
P
P
P
P
P
Congestion
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
P
Packet
Limited shared resources (buffers and links)
Design constraints: power, chip area, and timing
Notes: In modern multicore systems, NoC has limited shared resources due to various design constraints, such as power, chip area and timing.
Therefore, Noc will sometimes experience network congestion when there is a large amount of traffic.
Network congestion reduces network throughput, and hence application performance.
Here is a quick illustration on showing how congestion can occur in a network. Four different nodes send their packets (the red packets) to a central node.
since there is no free output link at the central node, the yellow packet cannot be injected into the network, which produces congestion.
------------------------------------------------------------------------------------------------
Injection only when output link is free. Put this in the slide?
Network congestion has detrimental an effect on the system performance.
--------------
Content: Higher network load leads to more congestion

## Slide 227: Goal
Improve performance in a highly congested NoC
Reducing network load decreases network congestion, hence improves performance
Approach: source throttling to reduce network load
  Temporarily delay new traffic injection
Naïve mechanism: throttle every single node
Notes: In this work, our goal is to improve application performance in a highly congested noc.
To achieve this, we observe that reducing network load leads to lower network congestion, hence improving performance.
To reduce network load, we take the approach of source throttling, which temporarily delays new traffic injection.
Although packet injections are delayed due to throttling, performance can still be improved b/c of less congestion in the network.
A naïve way of source throttling is to block injection of every node. However, this does not work well.
Now we will go through some key observations on how to design high-performance source throttling mechanism.
Soft throttling: inject with non-zero probability
Throttling rate: 0% (unthrottled) <-> 100% (fully blocked)
Key question:
Which application to throttle?
How aggressive do we throttle them?

## Slide 228: Key Observation #1
Chart: Normalized Performance
| mcf | gromacs | system
Throttle gromacs | 1 | 0.96 | 0.98
Throttle mcf | 1.05 | 1.14 | 1.09
gromacs: network-non-intensive
+ 9%
- 2%
Different applications respond differently to changes in network latency
mcf: network-intensive
Throttling mcf reduces congestion
gromacs is more sensitive to network latency
Throttling network-intensive applications benefits system performance more
Notes: Our first key observation is that different apps…..
To illustrate this point, we set up an experiment with a 16-node system running 8 copies of gromacs, which is a network-non-intensive spec benchmark,
and 8 copies of mcf, which is a network-intensive spec benchmark.
The figure shows the performance of this workload when different app is throttled at a fixed throttling rate.
The blue bar corresponds to throttling only gromcas
and the red bar corresponds to throttling only mcf
The yaxis indicate normalized performance to the baseline without throttling.
The xaxis shows three throughput measurements
The figure shows that when ONLY gromacs is throttled, the average system performance actually decreases by 2%,
On the other hand, when mcf is throttled the average perf increases by 9%.
This is because throttling mcf, which is network instensive, “significantly” reduces network load, and
it allows gromacs to make much faster progress with less latency since it’s more sensitive to latency.
**** Allowing gromacs to send packets with less latency is more beneficial because gromacs injects fewer number of packets and each packet represents a greater forward progress for the application ****
X: Therefore, non-intensive application is more sensitive to increases in network latency.
In the sum, throttling network-intensive applications benefits system performance more than ….
Gromacs:
1) not only do we not reduce congestion, but we also decrease performance by 2%
2)
Delete lines:
gromacs benefits more from reduced network latency
gromacs injects fewer packets, thus each packet represents a greater forward progress

## Slide 229: Key Observation #2
Chart: Throttling Rate (%)
| 80 | 82 | 84 | 86 | 88 | 90 | 92 | 94 | 96 | 98 | 100
Workload 1 | 9.6783 | 9.6962 | 9.7273 | 9.7829 | 9.8607 | 9.9987 | 10.286 | 10.713 | 9.5421 | 7.5361
Workload 2 | 10.3198 | 10.3497 | 10.3935 | 10.4632 | 10.6088 | 10.8432 | 11.1523 | 10.9859 | 9.6724 | 7.6214
Workload 3 | 14.5502 | 14.5837 | 14.6565 | 14.7872 | 15.0076 | 15.2556 | 15.1927 | 14.4139 | 12.8768 | 10.7685
Different workloads achieve peak performance at different throttling rates
Dynamically adjusting throttling rate yields better performance than a single static rate
90%
92%
94%
Notes: Our second key observation is that ….
To illustrate the benefits of using different throttling rate,
we evaluate system performance of three heterogeneous application workloads on a 16-core system with varying throttling rate.
The yaxis indicates sys perf in terms of WS
X-axis: shows the static throttling rate applied to each workload.
As we can see, different workloads require different throttling rate to achieve peak performance (in the example, 94% for wk1)
As a result, dynamically adjusting throttling rate yields better perf than a single static rate.

## Slide 230: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: Next we will talk about our mechanism which is built on top of these key observations.

## Slide 231: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjusts throttling rate to adapt to different workloads
Notes: Putting these observations together, we propose a new source throttling mechanism called Heterogeneous Adaptive Throttling (HAT)
There are two key components:
The first key component is app-aware throttling.
HAT throttles network-intensive apps that interfere with network-non-intensive applications to reduce network congestion
X: and allow non-intensive app to make faster forward progress.
2.The second key component is network-load….
HAT … read bullet, so that it provides high performance

## Slide 232: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjusts throttling rate to adapt to different workloads
Notes: Next I will talk about how HAT achieves app-aware throttling

## Slide 233: Application-Aware Throttling
Measure Network Intensity Use L1 MPKI (misses per thousand instructions) to estimate network intensity
Classify Application
  Sort applications by L1 MPKI
Throttle network-intensive applications
App
Σ MPKI < NonIntensiveCap
Network-non-intensive
Network-intensive
Higher L1 MPKI
Throttle
Notes: To perform app throttling, HAT first measures each application’s network intensity.
Since NoC primarily serves L1 cache misses in our evaluated system, we use L1 MPKI as a proxy to intensity.
  Once applications’ intensity is measured,
  HAT needs to classify applications as network-intensive or network-non intensive.
  To do so, HAT first sorts apps by their measured L1 MPKI. Next starting from the least mpki app,
  the applications are classified as network non intensive until their sum of MPKI exceeds a pre-set threshold,
  which we call it NonIntensiveCap.
  CAP ensures that the traffic of non-intensive applications provides sufficient load without causing severe network congestion.
  So it should be scaled with network capacity and tuned for the particular network design.
  All remaining applications are then considered as network intensive.
  When all applications are classified, HAT applies throttling to network-intensive applications.
  ****** KEY idea again*******
  Again, the reason to throttle them is to reduce congestion and allow non-intensive app,
  which are more sensitive to network latency, to send packets through the network more quickly.
  X: because a singe packet of a net-non-intensive app represents a greater forward progress,
  so throttling intensive app allows non-intensive app to get through the network more quickly.

## Slide 234: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjusts throttling rate to adapt to different workloads
Notes: Now we will talk about the second key component of HAT

## Slide 235: Dynamic Throttling Rate Adjustment
For a given network design, peak performance tends to occur at a fixed network load point
Dynamically adjust throttling rate to achieve that network load point
Notes: We observe that *PT1.
Thus, we dyn****
In our work, we empirically determine the peak network load point.

## Slide 236: Dynamic Throttling Rate Adjustment
Goal: maintain network load at a peak performance point
Measure network load
Compare and adjust throttling rate
  If network load > peak point:
  Increase throttling rate
  elif network load ≤ peak point:
  Decrease throttling rate
Notes: To achieve the goal of maintaining ….
HAT performs the following operations.
First it measures network load
HAT compares the current network load with the peak point and adjust throttling rate accordingly.
Increase th rate to reduce network load
Else…. Rate to allow more traffic to inject into the network

## Slide 237: Epoch-Based Operation
Continuous HAT operation is expensive
Solution: performs HAT at epoch granularity
Time
Current Epoch
(100K cycles)
Next Epoch
(100K cycles)
During epoch:
Measure L1 MPKI of each application
Measure network load
Beginning of epoch:
Classify applications
Adjust throttling rate
Reset measurements
Notes: Since continuously performing HAT’s operations is expensive,
we want to reduce the computation overhead by performing HAT at epoch gran.
Epoch length is 100K cycles
During an epoch….
Once an epoch finishes, hat uses these measurements to classify applications, and adjust throttling rate.
At the end, we reset the monitor counters to start new measurements.

## Slide 238: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: To this end, we have presented HAT.
Now let’s take a look at prior works

## Slide 239: Prior Source Throttling Works
Source throttling for bufferless NoCs [Nychis+ Hotnets’10, SIGCOMM’12]
  Application-aware throttling based on starvation rate
  Does not adaptively adjust throttling rate
  “Heterogeneous Throttling”
Source throttling off-chip buffered networks [Thottethodi+ HPCA’01]
  Dynamically trigger throttling based on fraction of buffer occupancy
  Not application-aware: fully block packet injections of every node
  “Self-tuned Throttling”
Notes: Here are two prior source throttling works that we will compare to in our evaluations.
The first work by Nychis et al. proposes source throttling for bufferless NoCs.
In particular, they propose an application-aware throttling based on starvation rate, which is metric they use to make throttling decision.
However, their mechanism does not adaptively adjust throttling rate based on network load.
We will call this work heterogeneous throttling for short in the evaluation section
The second work by thottethodi proposes source throttling for off-chip
It dynamically triggers throttling based on buffer occupancy.
One disadvantage of this work is that it is not app-aware, and it fully blocks packet injections of every node
Although it’s not originally designed for NoC, we still adapt it to NoC for comparison.
We will call this work self-tuned for short in the eval section.

## Slide 240: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: Now let’s take a look at our results

## Slide 241: Methodology
Chip Multiprocessor Simulator
  64-node multi-core systems with a 2D-mesh topology
  Closed-loop core/cache/NoC cycle-level model
  64KB L1, perfect L2 (always hits to stress NoC)
Router Designs
  Virtual-channel buffered router: 4 VCs, 4 flits/VC [Dally+ IEEE TPDS’92]
  Bufferless deflection routers: BLESS [Moscibroda+ ISCA’09]
Workloads
  60 multi-core workloads: SPEC CPU2006 benchmarks
  Categorized based on their network intensity
    Low/Medium/High intensity categories
Metrics: Weighted Speedup (perf.), perf./Watt (energy eff.), and maximum slowdown (fairness)
Notes: Here is our methodology.
We simulate 64-node multi-core systems …
The CPU cores model stalls, and interact with the caches and network in a closed-loop way.
We eval our throttling mechanism on top of different router designs.
1.
We form 60 multi-core workloads using spec
For measuring performance, we use weighted speedup which has been shown to a good multicore throughput metric

## Slide 242: Performance: Bufferless NoC (BLESS)
Chart: Workload Categories
| HL | HML | HM | H | amean
BLESS | 39.5123 | 38.9303 | 25.2614 | 15.0946 | 29.2127
Hetero. | 40.5786 | 40.1135 | 26.1258 | 15.3219 | 30.0343
HAT | 43.2522 | 43.3974 | 28.1143 | 16.3917 | 32.2514
HAT provides better performance improvement than past work
Highest improvement on heterogeneous workload mixes
- L and M are more sensitive to network latency
7.4%
Notes: We will first present performance results on BUFFERLESS NOCs USING BLESS
Y-axis
X-axis different workload categories, each category contains 15 wklds
In each bar group, the blue bar is for the baseline system without any throttling.
The second red bar uses heterogeneous throttling proposed by Nychis et al..
The last green bar is HAT.
Sevaral observations can be made:
First, HAT CONSISTENLY provides…BLUE. On average it achieve 7.4% performance improvement over hetero.
Second, GREEN
b/c L & M intensity applications are more sensitive to network latency and can benefit more from reduced congestion.

## Slide 243: Performance: Buffered NoC
Chart: Workload Categories
| HL | HML | HM | H | amean
Buffered | 43.4324 | 42.8599 | 30.7187 | 20.7078 | 33.8653
Self-Tuned | 43.3173 | 42.7665 | 29.9213 | 20.454 | 33.5555
Hetero. | 43.7044 | 43.061 | 30.6928 | 20.9577 | 34.0367
HAT | 44.8544 | 44.8571 | 32.3874 | 20.9946 | 35.1869
Congestion is much lower in Buffered NoC, but HAT still provides performance benefit
+ 3.5%
Notes: Here we show the performance on buffered network.
In addition to HAT and hetero., we also show perf of self-tuned by thottethodi
We see similar perf trend as in bufferless noc. HAT consistently provides higher perf improvement over the previous designs
BLUE  3.5%
3. Little gain for self-tuned b/c it performs hard throttling by completely blocking traffic injection until congestion is cleared.
This will only temporarily reduces congestion, but congestion will return soon once packet injections are allowed again.

## Slide 244: Application Fairness
HAT provides better fairness than prior works
Chart: Normalized Maximum Slowdwon
| amean
BLESS | 1
Hetero. | 1.1176
HAT | 0.85144
Chart: 
| amean
Buffered | 1
Self-Tuned | 1.0066
Hetero. | 0.9967
HAT | 0.95261
- 15%
- 5%
Notes: Next we show that HAT does not unfairly penalize any application through throttling
By reducing congestion in the network, HAT is actually able to improve performance of maximum slowed down application.

## Slide 245: Network Energy Efficiency
Chart: Normalized Perf. per Wat
| BLESS | Buffered
Baseline | 1 | 1
HAT | 1.085 | 1.05
8.5%
5%
HAT increases energy efficiency by reducing congestion
Notes: In addition, we evaluate HAT’s effect on network energy efficiency
Y:
X:
We use an improved ORION power model to evaluate static and dynamic power consumed by the on-chip network.
On average, HAT increases energy efficiency by 8.5% and 5% for BLESS and buffered networks, respectively.
This is because HAT allows packets to traverse through the network more quickly with less congestion.
X: HAT shows better improvement on BLESS because dynamic power dominated the total power due to higher deflection rate.

## Slide 246: Other Results in Paper
Performance on CHIPPER
Performance on multithreaded workloads
Parameters sensitivity sweep of HAT
Notes: Here’s a highlight of other results in the paper.
We evaluate the performance of different throttling works on another bufferless router design called CHIPPER.

## Slide 247: Conclusion
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing performance
Observations:
1) Some applications are more sensitive to network latency than others 2) Applications must be throttled differently to achieve peak performance
Key Idea: Heterogeneous Adaptive Throttling (HAT) 1) Application-aware source throttling 2) Network-load-aware throttling rate adjustment
Result: Improves performance and energy efficiency over state-of-the-art source throttling policies
Notes: In conclusion,
We address the problem of network congestion.
We make two key observations in this work:
First, some apps are more sen to network latency than others
Second, apps ……
Based on these two key observations, we propose our source throttling mechanism called HAT, which has two key components:
First, HAT performs app-aware source throttling, which selectively throttles certain applications.
Second, HAT dynamically adjusts throttling rate based on network load to achieve good performance.
Our evaluation shows that HAT improves perf…..

## Slide 248: Throttling Based Fairness in NoCs
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)

## Slide 249: Slack-Driven Packet Scheduling
  Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Aergia: Exploiting Packet Latency Slack in On-Chip Networks" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 106-116, Saint-Malo, France, June 2010. Slides (pptx)

## Slide 250: Packet Scheduling in NoC
Existing scheduling policies
  Round robin
  Age
Problem
  Treat all packets equally
  Application-oblivious
Packets have different criticality
  Packet is critical if latency of a packet affects application’s performance
  Different criticality due to memory level parallelism (MLP)
All packets are not the same…!!!
Notes: There are two existing scheduling policies
RR {explain}
Age {explain}
  Lead to contradictory decision making between routers: packets from one application may be prioritized at one router, to be delayed at next.
Stress bullets of application-oblivious
Transition:
Lets look at the motivation behind our proposed application-aware policies

## Slide 251: MLP Principle
Latency ( )
Stall
Compute
Latency ( )
Latency ( )
Stall ( ) = 0
Packet Latency != Network Stall Time
Different Packets have different criticality due to MLP
Criticality( ) >
Criticality( ) >
Criticality( )
Notes: with MLP cores issue several memory requests in parallel in the hope of overlapping future load misses with current load misses.
First I show an application with high MLP, it does some computation and sends a bunch of packets(in this case three, green, blue, red).
The core stalls for the packets to return.
Note that blue packet’s latency is overlapped and hence it has much fewer stall cycles.
Stall cycles of red packet is 0 because its latency is completely overlapped.
Thus our first observation packet latency != NST and different packets have different stalll / impact on execution time

## Slide 252: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 253: What is Aérgia?
Aérgia is the spirit of laziness in Greek mythology
Some packets can afford to slack!

## Slide 254: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 255: Slack of Packets
What is slack of a packet?
  Slack of a packet is number of cycles it can be delayed in a router without (significantly) reducing application’s performance
  Local network slack
Source of slack: Memory-Level Parallelism (MLP)
  Latency of an application’s packet hidden from application due to overlap with latency of pending cache miss requests
Prioritize packets with lower slack

## Slide 256: Concept of Slack
Instruction
Window
Stall
Network-on-Chip
Load Miss
Causes
returns earlier than necessary
Compute
Slack ( ) = Latency ( ) – Latency ( ) = 26 – 6 = 20 hops
Execution Time
Packet( ) can be delayed for available slack cycles without reducing performance!
Causes
Load Miss
Latency ( )
Latency ( )
Slack
Slack
Notes: We have two cores, core A colored green and core B colored red

## Slide 257: Prioritizing using Slack
Core A
Core B
Packet | Latency | Slack
 | 13 hops | 0 hops
 | 3 hops | 10 hops
 | 10 hops | 0 hops
 | 4 hops | 6 hops
Causes
Causes
Load Miss
Load Miss
Prioritize
Load Miss
Load Miss
Causes
Causes
Interference at 3 hops
Slack( ) > Slack ( )
Notes: Now the packets B-1 and A-0 interfere in the network for 3 hops, and we can choose one over the other
A-0 has slack of 0 hops and B-1 has a slack of 6 hops
So we can Prioritize A-0 over B-1 to reduce stall cycles of Core-A without increasing stall cycles of Core-B

## Slide 258: Slack in Applications
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
50% of packets have 350+ slack cycles
10% of packets have <50 slack cycles
Non-critical
critical

## Slide 259: Slack in Applications
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
art | 67.34 | 78.35 | 86.47 | 91.15 | 93.69 | 95.3 | 96.4 | 97.21 | 97.89 | 98.49 | 98.96
68% of packets have zero slack cycles

## Slide 260: Diversity in Slack
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12

## Slide 261: Diversity in Slack
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12
Slack varies between packets of different applications
Slack varies between packets of a single application

## Slide 262: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 263: Estimating Slack Priority
Slack (P) = Max (Latencies of P’s Predecessors) – Latency of P
  Predecessors(P) are the packets of outstanding cache miss requests when P is issued
Packet latencies not known when issued
Predicting latency of any packet Q
  Higher latency if Q corresponds to an L2 miss
  Higher latency if Q has to travel farther number of hops
Notes: Difficult to predict packet latency
Predicting Max (Predecessors’ Latencies)
  Number of predecessors
  Higher predecessor latency if predecessor is L2 miss
Predicting latency of a packet P
  Higher latency if P corresponds to an L2 miss
  Higher latency if P has to travel farther number of hops

## Slide 264: Estimating Slack Priority
Slack of P = Maximum Predecessor Latency – Latency of P
Slack(P) =
  PredL2: Set if any predecessor packet is servicing L2 miss
  MyL2: Set if P is NOT servicing an L2 miss
  HopEstimate: Max (# of hops of Predecessors) – hops of P
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)

## Slide 265: Estimating Slack Priority
How to predict L2 hit or miss at core?
  Global Branch Predictor based L2 Miss Predictor
    Use Pattern History Table and 2-bit saturating counters
  Threshold based L2 Miss Predictor
    If #L2 misses in “M” misses >= “T” threshold then next load is a L2 miss.
Number of miss predecessors?
  List of outstanding L2 Misses
Hops estimate?
  Hops => ∆X + ∆ Y distance
  Use predecessor list to calculate slack hop estimate

## Slide 266: Starvation Avoidance
Problem: Starvation
  Prioritizing packets can lead to starvation of lower priority packets
Solution: Time-Based Packet Batching
  New batches are formed at every T cycles
  Packets of older batches are prioritized over younger batches

## Slide 267: Putting it all together
Tag header of the packet with priority bits before injection
Priority(P)?
  P’s batch (highest priority)
  P’s Slack
  Local Round-Robin (final tie breaker)
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)
Batch
(3 bits)
Priority (P) =
Notes: Say “older batches are prioritized over younger batches”

## Slide 268: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 269: Evaluation Methodology
64-core system
  x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  32KB private L1 and 1MB per core shared L2 caches, 32 miss buffers
  4GB DRAM, 320 cycle access latency, 4 on-chip DRAM controllers
Detailed Network-on-Chip model
  2-stage routers (with speculation and look ahead routing)
  Wormhole switching (8 flit data packets)
  Virtual channel flow control (6 VCs, 5 flit buffer depth)
  8x8 Mesh (128 bit bi-directional channels)
Benchmarks
  Multiprogrammed scientific, server, desktop workloads (35 applications)
  96 workload combinations
Notes: We do our evaluations on a detailed cycle accurate CMP simulator with state-of-art NoC model.
Our evaluations are across 35 diverse applications.
Our results are for 96 workload combinations.

## Slide 270: Qualitative Comparison
Round Robin & Age
  Local and application oblivious
  Age is biased towards heavy applications
Globally Synchronized Frames (GSF) [Lee et al., ISCA 2008]
  Provides bandwidth fairness at the expense of system performance
  Penalizes heavy and bursty applications
Application-Aware Prioritization Policies (SJF) [Das et al., MICRO 2009]
  Shortest-Job-First Principle
  Packet scheduling policies which prioritize network sensitive applications which inject lower load
Notes:     Age
    heavy applications flood the network
    higher likelihood of an older packet being from heavy application
GSF
    Each application gets equal and fixed quota of flits (credits) in each batch.
    Heavy application quickly run out of credits after injecting into all active batches & stall till oldest batch completes and frees up fresh credits.
    Underutilization of network resources

## Slide 271: System Performance
SJF provides 8.9% improvement in weighted speedup
Aérgia improves system throughput by 10.3%
Aérgia+SJF improves system throughput by 16.1%
Chart: Normalized System Speedup
Age | 1
RR | 1.0046
GSF | 0.88979
SJF | 1.0949
Aergia | 1.1084
SJF+Aergia | 1.1668

## Slide 272: Network Unfairness
SJF does not imbalance network fairness
Aergia improves network unfairness by 1.5X
SJF+Aergia improves network unfairness by 1.3X
Chart: Network Unfairness
Age | 10.21
RR | 10.64
GSF | 10.4794
SJF | 9.8747
Aergia | 6.78
SJF+Aergia | 7.9

## Slide 273: Conclusions & Future Directions
Packets have different criticality, yet existing packet scheduling policies treat all packets equally
We propose a new approach to packet scheduling in NoCs
  We define Slack as a key measure that characterizes the relative importance of a packet.
  We propose Aérgia a novel architecture to accelerate low slack critical packets
Result
  Improves system performance: 16.1%
  Improves network fairness: 30.8%

## Slide 274: Slack-Based Packet Scheduling
Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Aergia: Exploiting Packet Latency Slack in On-Chip Networks" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 106-116, Saint-Malo, France, June 2010. Slides (pptx)

## Slide 275: Express-Cube Topologies
  Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Express Cube Topologies for On-Chip Interconnects" Proceedings of the 15th International Symposium on High-Performance Computer Architecture (HPCA), pages 163-174, Raleigh, NC, February 2009. Slides (ppt)

## Slide 276: 2-D Mesh

## Slide 277: 2-D Mesh
Pros
  Low design & layout complexity
  Simple, fast routers
Cons
  Large diameter
  Energy & latency impact

## Slide 278: Concentration (Balfour & Dally, ICS ‘06)
Pros
  Multiple terminals attached to a router node
  Fast nearest-neighbor communication via the crossbar
  Hop count reduction proportional to concentration degree
Cons
  Benefits limited by crossbar complexity

## Slide 279: Concentration
Side-effects
  Fewer channels
  Greater channel width

## Slide 280: Replication
CMesh-X2
Benefits
  Restores bisection channel count
  Restores channel width
  Reduced crossbar complexity

## Slide 281: Flattened Butterfly (Kim et al., Micro ‘07)
Objectives:
  Improve connectivity
  Exploit the wire budget

## Slide 282: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 283: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 284: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 285: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 286: Flattened Butterfly (Kim et al., Micro ‘07)
Pros
  Excellent connectivity
  Low diameter: 2 hops
Cons
  High channel count: k2/2 per row/column
  Low channel utilization
  Increased control (arbitration) complexity

## Slide 287: Multidrop Express Channels (MECS)
Objectives:
  Connectivity
  More scalable channel count
  Better channel utilization

## Slide 288: Multidrop Express Channels (MECS)

## Slide 289: Multidrop Express Channels (MECS)

## Slide 290: Multidrop Express Channels (MECS)

## Slide 291: Multidrop Express Channels (MECS)

## Slide 292: Multidrop Express Channels (MECS)

## Slide 293: Multidrop Express Channels (MECS)
Pros
  One-to-many topology
  Low diameter: 2 hops
  k channels row/column
  Asymmetric
Cons
  Asymmetric
  Increased control (arbitration) complexity

## Slide 294: Partitioning: a GEC Example
MECS
MECS-X2
Flattened
Butterfly
Partitioned
MECS

## Slide 295: Analytical Comparison
 | CMesh |  | FBfly |  | MECS | 
Network Size | 64 | 256 | 64 | 256 | 64 | 256
Radix (conctr’d) | 4 | 8 | 4 | 8 | 4 | 8
Diameter | 6 | 14 | 2 | 2 | 2 | 2
Channel count | 2 | 2 | 8 | 32 | 4 | 8
Channel width | 576 | 1152 | 144 | 72 | 288 | 288
Router inputs | 4 | 4 | 6 | 14 | 6 | 14
Router outputs | 4 | 4 | 6 | 14 | 4 | 4

## Slide 296: Experimental Methodology
Topologies | Mesh, CMesh, CMesh-X2, FBFly, MECS, MECS-X2
Network sizes | 64 & 256 terminals
Routing | DOR, adaptive
Messages | 64 & 576 bits
Synthetic traffic | Uniform random, bit complement, transpose, self-similar
PARSEC benchmarks | Blackscholes, Bodytrack, Canneal, Ferret, Fluidanimate, Freqmine, Vip, x264
Full-system config | M5 simulator, Alpha ISA, 64 OOO cores
Energy evaluation | Orion + CACTI 6

## Slide 297
64 nodes: Uniform Random

## Slide 298
256 nodes: Uniform Random

## Slide 299
Energy (100K pkts, Uniform Random)

## Slide 300
64 Nodes: PARSEC

## Slide 301: Summary
MECS
  A new one-to-many topology
  Good fit for planar substrates
  Excellent connectivity
  Effective wire utilization
Generalized Express Cubes
  Framework & taxonomy for NOC topologies
  Extension of the k-ary n-cube model
  Useful for understanding and exploring on-chip interconnect options
  Future: expand & formalize

## Slide 302: Scalability: Express Cube Topologies
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Express Cube Topologies for On-Chip Interconnects" Proceedings of the 15th International Symposium on High-Performance Computer Architecture (HPCA), pages 163-174, Raleigh, NC, February 2009. Slides (ppt)

## Slide 303: Kilo-NoC: Topology-Aware QoS
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees" Proceedings of the 38th International Symposium on Computer Architecture (ISCA), San Jose, CA, June 2011. Slides (pptx)

## Slide 304: Motivation
Extreme-scale chip-level integration
  Cores
  Cache banks
  Accelerators
  I/O logic
  Network-on-chip (NOC)
10-100 cores today
1000+ assets in the near future

## Slide 305: Kilo-NOC requirements
High efficiency
  Area
  Energy
Good performance
Strong service guarantees (QoS)

## Slide 306: Topology-Aware QoS
Problem: QoS support in each router is expensive (in terms of buffering, arbitration, bookkeeping)
  E.g., Grot et al., “Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip,” MICRO 2009.
Goal: Provide QoS guarantees at low area and power cost
Idea:
  Isolate shared resources in a region of the network, support QoS within that area
  Design the topology so that applications can access the region without interference

## Slide 307: Baseline QOS-enabled CMP
Multiple VMs
sharing a die
Shared resources
(e.g., memory controllers)
VM-private resources
(cores, caches)
QOS-enabled router
Q

## Slide 308: Conventional NOC QOS
Contention scenarios:
Shared resources
  memory access
Intra-VM traffic
  shared cache access
Inter-VM traffic
  VM page sharing

## Slide 309: Conventional NOC QOS
Contention scenarios:
Shared resources
  memory access
Intra-VM traffic
  shared cache access
Inter-VM traffic
  VM page sharing
Network-wide guarantees without network-wide QOS support

## Slide 310: Kilo-NOC QOS
Insight: leverage rich network connectivity
  Naturally reduce interference among flows
  Limit the extent of hardware QOS support
Requires a low-diameter topology
  This work: Multidrop Express Channels (MECS)
  Grot et al., HPCA 2009

## Slide 311: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference
QOS-free

## Slide 312: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 313: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 314: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 315: Kilo-NOC view
Topology-aware QOS support
  Limit QOS complexity to a fraction of the die
Optimized flow control
  Reduce buffer requirements in QOS-free regions
QOS-free

## Slide 316: Evaluation Methodology
Parameter | Value
Technology | 15 nm
Vdd | 0.7 V
System | 1024 tiles: 256 concentrated nodes (64 shared resources)
Networks: | 
MECS+PVC | VC flow control, QOS support (PVC) at each node
MECS+TAQ | VC flow control, QOS support only in shared regions
MECS+TAQ+EB | EB flow control outside of SRs, Separate Request and Reply networks
K-MECS | Proposed organization: TAQ + hybrid flow control

## Slide 317: Area comparison

## Slide 318: Energy comparison

## Slide 319: Summary
Kilo-NOC: a heterogeneous NOC architecture for kilo-node substrates
Topology-aware QOS
  Limits QOS support to a fraction of the die
  Leverages low-diameter topologies
  Improves NOC area- and energy-efficiency
  Provides strong guarantees

## Slide 320: Low-Cost QoS in On-Chip Networks (II)
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees" Proceedings of the 38th International Symposium on Computer Architecture (ISCA), San Jose, CA, June 2011. Slides (pptx)